## Slide 1: Determining Bounds on Execution Times
Jung Chanmin
06.09.27

## Slide 2: Index
Abstract
Introduction
Cache Behavior Prediction
Pipeline Analysis
Path Analysis Using Integer Linear Programming
Q&A (not recommend)

## Slide 3: Abstract
Run-time guarantees play an important role in the area of Embedded System. (hard real time)
  Schedulability analysis has to be performed.
  Schedulability analysis require upper bounds for the execution times of all task in the system.
  The bounds must be Safe and Tight.
Modern MP architecture is so~ complex
   hard to analysis of the timing behavior of instructions
How to compute safely & precise bounds on the execution times~

## Slide 4: Introduction
Upper Bounds (WCETs)!!  Key Factor
  It has to be Safe~! & Tight~!
The state space is too large to explore all possible executions, So! Determine the exact Worst, best-case execution times.

## Slide 5: Introduction (cont)
In modern MP architectures cache, pipelines, and all kinds of speculation are key features for improving performance.  Complex~!
  The execution time of individual instructions and the contribution of one execution of an instruction can vary widely.
Two cases
  The instruction goes smoothly through the pipeline
  Everything goes Wrong~

## Slide 6: Introduction (cont)

## Slide 7: Introduction (cont)
Timing accident
  Event that increase in execution time ex) cache miss
Timing penalty
  Additional Cycle ex) cache miss penalty
How to predict or exclude timing accidents
   needs information about the execution history
Excluding timing accidents = decreasing the upper bounds
  But! Exception case (timing anomaly)

## Slide 8: Introduction (cont)
Tool Architecture

## Slide 9: Introduction (cont)
Timing Anomalies
  Contra-intuitive influences of the local execution time of one instruction on the global execution time of the whole program
    Ex) a locally faster execution of an instruction can lead to a globally longer execution time of the whole program.
    Ex) a cache miss may actually speed up program exectution

## Slide 10: Cache-Behavior Prediction
Cache Memory
  Three parameters
    Capacity
    Block size
    Associativity
      Fully associative
        A block can reside in any cache location
      Direct mapped
        A block can reside in exactly one location
      X-way set associative
        A block can reside in exactly X locations

## Slide 11: Cache-Behavior Prediction
Cache Memory
  When the cache is full and the processor requests further data
     Replacement strategy
      LRU (Least Recently Used)
      FIFO (First In First Out)
      random

## Slide 12: Cache-Behavior Prediction
Cache Memory
  Use Fully associative caches with LRU replacement strategy in this paper

## Slide 13: Cache-Behavior Prediction
Abstract Semantics
  Must Analysis
    Determine a set of memory blocks that are in the cache at given program point
  May Analysis
    Determine all memory blocks that may be in the cache at a given program point

## Slide 14: Cache-Behavior Prediction
Abstract Semantics
  Must Analysis

## Slide 15: Cache-Behavior Prediction
Abstract Semantics
  May Analysis

## Slide 16: Pipeline Analysis
To find out how instructions move through the pipeline
  How many cycle they spend in the pipeline
Pipeline analysis regards abstract execution of sequences of instructions on abstract pipelines
   the execution of programs on abstract pipelines produces abstract traces ( sequences of abstract states )

## Slide 17: Pipeline Analysis
Simple Architecture without Timing Anomalies
  Simple Architecture
    With in-order execution
    Local worst case contribute to the program’s global execution time
    Safe to assume the local worst cases for unknown information

## Slide 18: Pipeline Analysis
Processors with Timing Anomalies
  Out-of-order execution
  Local worst cases contribute worst-case times of the global execution times  no more valid

## Slide 19: Pipeline Analysis
Pipeline Modeling
  The basis for pipeline analysis is a model of an abstract version of the processor pipeline
  Processors have concrete pipelines described in VHDL
  Eliminate many components of a concrete pipeline that are not relevant for the timing behavior
  Deriving an abstract pipeline is a complex task

## Slide 20: Pipeline Analysis
Pipeline Modeling
  The ColdFire MCF 5307 pipeline
    Fetch pipeline
      Fetches instructions form memory or the cache
    Execution pipeline
      Executes instructions

## Slide 21: Pipeline Analysis
Formal Models of Abstract Pipelines
  An abstract pipeline state consists of several units and signals
  Signals may be instantaneous or delayed
  The instantaneous signals between units are used to transport information between the units

## Slide 22: Path Analysis Using Integer Linear Programming
The structure of a program and the set of program paths can be mapped to an ILP in a very natural way
An ILP consists of two parts
  The cost function
  Constraints
Cost function  the number of CPU cycles
Variable  execution count of one basis block

## Slide 23: Summary
리얼타임에서 execution time의 bound를 정하는 것은 중요한 일이다. 하지만 시스템이 복잡해짐에 따라 bound를 정하는 것이 어려워지고 있다.
이 논문에서는 어떤 task의 execution time의 bound를 정하기 위해 3가지 분석방법을 제시한다.
  첫째. Cache prediction을 통한 분석
  둘째. PipeLine 분석
  셋째. ILP를 이용한 경로 분석

## Slide 24: 추가 설명!
지난 이야기
  Real-Time에서 execution time의 bound를 정하는 것은 중요한 일이다(hard real time). 하지만 시스템이 복잡해짐에 따라 bound를 정하는 것이 어려워지고 있다.
  이 논문에서는 어떤 task의 execution time의 bound를 정하기 위해 3가지 분석방법을 제시한다.
    Cache prediction을 통한 분석
    PipeLine을 통한 분석
    ILP를 이용한 경로 분석

## Slide 25: Cache Prediction을 통한 분석
How to statically precompute cache contents
  Must Analysis
    For each program point (and calling context), find out which blocks are in the cache.
  May Analysis
    For each program point (and calling context), find out which blocks may be in the cache
      Complement says what is not in the cache

## Slide 26: Cache Prediction을 통한 분석
Must-Cache and May-Cache Information
  Must Analysis determines safe information
  about cache hits
    Each predicted cache hit reduces WCET
  May Analysis determines safe information
  about cache misses
    Each predicted cache miss increases BCET

## Slide 27: Cache Prediction을 통한 분석
Cache Analysis : Join (Must)

## Slide 28: Cache Prediction을 통한 분석
Cache Analysis : Join (May)

## Slide 29: Cache Prediction을 통한 분석
Contribution to WCET
  Information about cache contents sharpens timings

## Slide 30: Pipeline을 통한 분석
How to create a pipeline analysis
  Starting point: Concrete model of execution
  First build reduced model
  Then build abstract timing model

## Slide 31: Pipeline을 통한 분석

## Slide 32: Pipeline을 통한 분석
Abstract Instruction-Execution

## Slide 33: ILP를 이용한 경로 분석
ILP solver maximizes this function to determine the WCET

## Slide 34: ILP를 이용한 경로 분석
Example (simplified constraints)

## Slide 35: Q&A

## Slide 36: Quiz
Q1. Cache prediction 방식에서 사용하는 analysis방식 2가지를 제시하고 이것이 궁극적으로 뜻하는 바가 무엇인지 서술 하시오.
A1. Must analysis 방식과 May analysis 방식이 있으며 전자분석 방식은 Cache안에 특정 block이 존재한다는 hit에 관한 정보를 알려주는 분석이며 후자는 분석결과 나온 cache안의 block 이외의 것을 참조하면 항상 cache miss가 난다는 것을 알려주는 분석이다.

## Slide 37: Quiz (cont’d)
Q2. 다음 그림은 ILP를 이용한 Path analysis 방식이다. 여기서 a의 실행 회수가 1일때 Worst Case Execution Time 을 아래 공식을 이용하여 구하여라.
공식

## Slide 38: Quiz (cont’d
A2. 방정식의 해를 구하면 각 block의 실행회수는 오른쪽 하단과 같다. 그러므로 a한번 b한번 f를 한번 실행하여 수행하는 것이 19cycles로 가장 worst case execution time를 가진다.