## Slide 1: Interface Specification and Converter Synthesis
Hanyang Univ.
ESOC
Young Geun Lee

## Slide 2: Outline
Introduction
Automata-Based Converter Synthesis
  Interface Specification
  Requirements Specification
  Synthesis
Algebraic Formulation
  Trace-Based Solution
  End-to-End Specification
Conclusion

## Slide 3: Introduction
Reuse is a design technique to reduce the complexity of designing a system.
A design process can be simplified by using a methodology that promotes the reuse of existing components, also known as IPs.
  Unforeseen interactions may often make the behavior of the resulting design unpredictable.
  Interfaces are used to ensure the compatibility between components.
Notes: 2. Design rules have been proposed
- 동작하고자 하는 환경에 대해 수많은 가정을 만들고 개개인의 요소들이 어떻게 동작하는지 확인
- extensive simulation and prototyping 역시 불충분하다 compositions이 여전히 필요

## Slide 4: Introduction(cont.)
When components are taken from legacy systems or from third-party vendors, interface protocols are unlikely to be compatible.
  Approaches have been proposed that adapt the components by constructing a converter among the incompatible communication protocols.
The problem of converting one protocol into another can be addressed.
  By considering their conjunction in terms of the product of the corresponding automata.
  By removing the states and transitions that lead to a violation of one of the two protocols.
The converter uses state information to rearrange the communication between the original interfaces, in order to ensure compatibility.
Notes: 3. Converter 메시지의 시간은 변화시킬 수 있으나, 순서는 바꿀 수 없다. N-bounded buffer을 사용하여

## Slide 5: Automata-Based Converter Synthesis
Set up the conversion problem for send-receive protocols, where the sender and the receiver are specified as automata.
A third automaton, the requirement, is also introduced to specify constraints on the converter, such as buffer size and the possibility of message loss.

## Slide 6: Interface Specification
Notes: The symbols a and b are used to denote the first and the second part of the data, respectively.
The symbol T denotes instead the absence or irrelevance of the data. In other words, it acts as a don’t care.
The producer (handshake) protocol : because it could negotiate when to send the second part of the data. After b is transmitted, the protocol returns to its initial state, and is ready for a new transaction.
The receiver (serial) protocol : because it requires a and b to be transferred back-to-back.

## Slide 7: Interface Specification(cont.)
The interface of the producer is defined so that it can wait an unbounded amount of time between the two parts.
The interface of the consumer is defined so that it requires that once the first part has been received, the second is also received during the state transition that immediately follows the first.
The two protocols are incompatible.
An intermediate converter must be inserted to make the communication possible.

## Slide 8: Interface Specification(cont.)
The two sets of signals are different and should be connected through a converter.
The specification merely defines the (partial) order in which the symbols can be presented to and produced by the converter.
Notes: 2. It is possible to explicitly represent the values passed; this is necessary when the behavior of the protocols depends on the data, or when the data values provided by one protocol must be modified (translated) before being forwarded to the other protocol.

## Slide 9: Requirements Specification
Inputs and outputs of protocols, specification,
and converter

## Slide 10: Requirements Specification(cont.)
The specification accepts inputs a, b, a’, b’, and acts as a global observer that states what properties the converter should have.
a and b are the converter inputs, and a’, b’ its outputs.

## Slide 11: Requirements Specification(cont.)
Specification automaton
Notes: The specification 은 a, b 의 순서가 바뀌는 것을 허락한다.
A, b 가 항상 쌍으로 나올 필요 없다.
a’ 은 a보다 먼저 생기면 안 된다.
A’ 은 새로운 a나 b가 발생하면 생겨야 한다.
In fact, we can view the specification as an observer that specifies what can happen (a transition on some symbol is available) and what should not happen ( a transition on some symbol is not available).

## Slide 12: Requirements Specification(cont.)
This specification states that no symbols should be discarded or duplicated by the converter.
Symbols must be delivered in the same order in which they were received.
The converter can store at most one undelivered symbol at any time.
State 0 denotes the case in which all received symbols have been delivered (or that no symbol has been received, yet).
State a denotes the case in which symbol a has been received, but it has not been output yet.
Similarly, State b denotes the case in which symbol b has been received, but not yet output.
Notes: The alphabet of the automaton is derived from the Cartesian product of the alphabets of the two protocols for which we want to build a converter.

## Slide 13: Synthesis (Composition between handshake and serial)
Notes: The direction of the signals is reversed; the inputs to the protocols become the outputs of the converter, and vice versa.
This composition is also a specification for the converter, since on both sides the converter must comply with the protocols that are being interfaced.
However this specification does not have the notion of synchronization (partial order, or causality constraint)

## Slide 14: Synthesis(cont.)
The direction of the signals is reversed.
This composition is also a specification for the converter.
However this specification does not have the notion of synchronization.
The converter satisfies both specifications
  By taking the converter to be the composition of the product machine with the specification.
  By removing transitions that violate either protocol or the correctness specification.
Notes: the inputs to the protocols become the outputs of the converter, and vice versa.
2. since on both sides the converter must comply with the protocols that are being interfaced.
3. (partial order, or causality constraint)

## Slide 15: Synthesis (Converter computation, phase 1)
Notes: Transitions can be removed from the composition only if doing so dose not result in an assumption on the behavior of the sender.

## Slide 16: Synthesis (Converter computation, phase 2)

## Slide 17: Synthesis (Converter computation, phase 3)
Notes: The resulting machine has now no illegal transitions.
This machine complies both with the specification and with the two protocols, and thus represents the correct conversion (correct relative to the specification).
Notice how the machine at first stores the symbol a without sending it ( transition a/T’). Then, when b is received, the machine sends a’, immediately followed in the next cycle by b’, as required by the serial protocol.

## Slide 18: Algebraic Formulation (Background) - Inverse Delete -
T1 = <I1,O1,S1,F1> and T2 = <I2,O2,S2,F2>
If N is signals in A2 and not in A1, then add N to I1 and extend S1 and F1 to allow events on signals in N at any time. ( A = I∪O, P = S∪F )
This function can be extended to a trace structure as follows:
  del(N)-1(T) = <I∪N,O,del(N)-1(S),del(N)-1(F)>

## Slide 19: Algebraic Formulation (Background) - Composition -
Given two trace structures with consistent signal sets(A1 = A2 and O1∩O2 = ø)
  T1 ∩ T2 = <I1∩I2, O1∪O2, S1∩S2, (F1∩P2)∪(F2∩P1)>
T1 || T2 = del(A2-A1)-1(T1) ∩ del(A1-A2)-1(T2)
Parallel composition
  If T1 = (S1, F1) and T2 = (S2, F2), then the parallel composition T = T1 || T2 is given by
  T = (S1∩ S2, (F1 ∩(S2 ∪ F2)) ∪ (F2 ∩(S1 ∪ F1 )))

## Slide 20: Algebraic Formulation (Background) - Conformation & Mirror & Projection -
To verify that a circuit correctly implements a specification, we must show that TI conforms to TS (denoted TI ≤ TS)
  TA ≦ TB whenever SA ∪ FA ⊆ SB ∪ FA and FA ⊆ FB
The complement of T is defined as the most general component that can be composed with T without generating any failure.
  Mirror(T) = (S-F, ( S ∪ F)’)
proj({a})(<a, b, a, T, b, a, b, b, a, …>) = <a, T, a, T, T, a, T, T, a, …>

## Slide 21: Trace-Based Solution
The problem consists of finding a local specification L for X, such that if X implements L, then the full implementation I implements the global specification G.
P1 || X || P2 ≦ G
Notes: G : a global specification
P1, P2 : a partial implementation, call a context, which consists of the composition of several modules
The implementation is only partially specified, and is completed by inserting an additional module X to be composed with the rest of the context.

## Slide 22: Trace-Based Solution(cont.)
The problem of local specification synthesis is set up as usual as the equation
  Proj(A)(P1 || P2 || X) ≦ G
  The operator proj(A), whose effect is to retain only the elements of the alphabet that are contained in the set A.
The solution to the equation is expressed in the form
  C ≦ mirror(Proj(A)(P1 || P2 || mirror(G)) )
  Mirror is a generalized complementation operation.

## Slide 23: Trace-Based Solution(cont.)
The sender protocol and the specification aren’t needed to add failures.
The receiver must be augmented with a state representing the failure traces.
P1 : the sender protocol, P2 : the receiver, C : the converter, G : the specification
  P1 || P2 || C ≦ G
  C ≦ mirror(P1 || P2 || mirror(G))
  Projections are not needed in this case, since the alphabet is always A = {T, a, b, T’, a’, b’} which is also the alphabet C.
Notes: Since they have only outputs and therefore do not constrain the environment in any way.
A transition to this additional state is taken from each state on all the inputs for which an action is not already present.

## Slide 24: Trace-Based Solution(cont.)
After taking the complementation, the resulting component may not be receptive.
This can be avoided by applying the operations of autofailure manifestation and failure exclusion before computing the mirror.
  A state is an autofailure if all its outgoing transitions are failures. In that case, the state can be bypassed by directing its incoming transitions to the outgoing failure state
  Failure exclusion : Remove from success set any trace which is also a failure (S = S - F)
For a deterministic and receptive automaton the mirror can be computed by removing the existing outgoing failure transitions of each state and by adding transitions to a new failure state for each of the input actions that does not already result in a success.
Notes: 2.2 whenever they are matched by a corresponding failure transition on the same input in the same state.
3. We obtain exactly the result depicted in Figure 23.7, with additional failure transitions that stand to represent the flexibility in the implementation.

## Slide 25: Adding transitions to a new failure state
Input b
Input b
Input a
Notes: The resulting machine has now no illegal transitions.
This machine complies both with the specification and with the two protocols, and thus represents the correct conversion (correct relative to the specification).
Notice how the machine at first stores the symbol a without sending it ( transition a/T’). Then, when b is received, the machine sends a’, immediately followed in the next cycle by b’, as required by the serial protocol.

## Slide 26: End-to-End Specification
The global specification may be limited to talking about the behavior of the communication channel as a whole.
It would be independent of the particular signals employed internally by each protocol.

## Slide 27: End-to-End Specification(cont.)
The sender protocol
Input signal : ft (set to 1 when data is available)
Output signal : st (clock the serial delivery of the data), sd (the data)

## Slide 28: End-to-End Specification(cont.)
Input signal : rt (synchronize the start of the serial transfer with the other protocol), rd
Output signal : tt (inform the environment when new data is available)
The receiver fails if the second bit of the data is not received within the clock cycle that follows the delivery of the first bit.
The receiver protocol

## Slide 29: End-to-End Specification(cont.)
The global specification

## Slide 30: End-to-End Specification(cont.)
The global specification has the same inputs as the sender protocol, and the same outputs as the receiver protocol.
A trace is successful if a certain value is received on the sender side, and the same value is emitted immediately or after an arbitrary delay on the receiver side.
The specification fails if a new data value is received while the old value has not been delivered yet.

## Slide 31: End-to-End Specification(cont.)
The local converter specification
Notes: The converter that we obtain is nondeterministic and could take paths that are “slower” than one could expect them to be.

## Slide 32: End-to-End Specification(cont.)
The converter makes sure that the correct data is transferred from one end to the other.
An important side effect of the specific choice of synchronous model : deadlock situation
  Avoid a failure by withholding an input
  “stopping time” before reaching the deadlock state
  Consider deadlock states tantamount to an autofailure, and remove them from the final result.

## Slide 33: End-to-End Specification(cont.)
The optimized converter

## Slide 34: End-to-End Specification(cont.)
A “faster” implementation can be obtained by selecting the appropriate paths whenever a choice is available.
The converter starts the transfer in the same clock cycle in which the last bit from the sender protocol is received.

## Slide 35: Conclusions
Emerging new design methodologies promote reuse of intellectual property as one of the basic techniques to handle complexity in the design process.
In a methodology based on reuse, the components are predesigned and precharacterized, and are assembled in the system to perform the desired function.
System verification reduces to the verification of the interaction of the components used in the system.

## Slide 36
Q & A