## Slide 1: Embedded Systems CHAPTER 2: Real-Time in Embedded Systems
CAD & SoC Lab.
1st Hong Gi Hoon

## Slide 2: Contents
2.1 Introduction
2.2 Design of RTSs
2.3 Real-Time Operating Systems
2.4 Real-Time Scheduling
2.5 Real-Time Communications

## Slide 3: 2.1 Introduction
There is no commonly agreed upon definition fo what a RTS is, but the following characterization is (almost) universally accepted:
  RTSs are computer systems that physically interact with the real world.
  RTSs have requirements on the timing of these interactions.
Real-time requirements typically express that an interaction should occur within specified timing bound. This is quite different from requiring the interaction to be as fast as possible.

## Slide 4: 2.1 Introduction
Hard- and Soft- RTSs
  A system that is designed to meet strict timing requirements is often referred to as a hard RTS.
    Ex) engine control system
  In contrast, systems for which occasional timing failures are acceptable are termed soft RTS.
    Ex) banking system

## Slide 5: 2.2 Design of RTSs
This section presents some important architectural issues for embedded RTSs, together with some supporting commercial tools.

## Slide 6: 2.2.1 Reference Architecture
Figure 2.1 is a model of any computer-based system interacting with an external environment via sensors and actuators.
The simplest RTS is a single processor, but in many cases the RTS is a distributed computer system consisting of a set of processors interconnected by a communications networks.

## Slide 7: 2.2.2 Models of Interaction
component
  any type of software unit, such as a task or a module
predictable and unpredictable models
  Predictable models are have a more predictable and robust behavior with respect to timing than other models.
    Pipes-and-filters
    Publisher-subscriber
    Blackboard
  Unpredictable models increase the (timing) unpredictability of the system.
    Client-server
    Message boxes

## Slide 8: 2.2.2 Models of Interaction
2.2.2.1 Pipes-and-Filters
  In this model, both data and control flow is specified using input and output ports of components.
2.2.2.2 Publisher-Subscriber
  The publisher-subscriber model is similar to the pipes-and-filters model but it usually decouples data and control flow.
2.2.2.3 Blackboard
  The blackboard model allows variables to be published on a globally available balckboard area.

## Slide 9: 2.2.2 Models of Interaction
2.2.2.4 Client-Server
  In the client-server model, a client asynchronously invokes the service of a server.
  The client-server model has inherently unpredictable timing. Since services are invoked asynchronously.
2.2.2.5 Message Box
  A component can have a set of message boxes, and components communicate by posting messages in each other message boxes.

## Slide 10: 2.2.3 Execution Strategies
Two main execution paradigms for RTSs:
  Time-triggered and event-triggered
  Time-triggered:
    When using timed-triggered execution, activities occur at predefined instances of time.
  Event-triggered:
    In an event-triggered execution, actions are triggered by event occurrences.
  Time-triggered dependability and event-triggered flexibility.

## Slide 11: 2.2.4 Component-Based Design
In CBD, a software component is used to encapsulate some functionality. That functionality is only accessed through the interface of the component. A system is composed by assembling a set of components and connecting their interfaces.

## Slide 12: 2.2.5 Tools for Design of RTSs
UML (United Modeling Language)
  UML’s focus is mainly on client-server solutions, and it has proven inapt for RTSs design.
extend UML
  Extend UML with constructs suitable for real-time programs have emerged.
SDL
  The fundamental model of computation is the message-box model.
For more resource constrained hard RTSs
  Arcticus System, TTTech, and Vector
UML2
  Within the near future UML2 will become an adopted standard.

## Slide 13: 2.3 Real-Time Operating Systems
Using a general-purpose OS when developing RTSs has several drawbacks:
  High resource utilization
  Difficult to access hardware and devices in a timely manner
  Lack of services to allow timing sensitive interactions between different processes.

## Slide 14: 2.3.1 Typical Properties of RTOSs
As a general rule of thumb one can say that RTOSs are:
  Suitable for resource constrained environments.
  Giving the application programmer easy access to hardware features.
  Providing services that allow implementation of timing sensitive code.
  Tailored to fit the embedded systems development process.

## Slide 15: 2.3.2 Mechanisms for Real-Time
One of the most important functions of an RTOS is to arbitrate access to shared resources.
The two most obvious resource that the RTOS manages access to are:
  The CPU – that is, the RTOS should allow processes to execute in a predictable manner.
  Shared memory areas – that is, the RTOS should resolve contention to shared memory in a way that gives predictable timing.

## Slide 16: 2.3.2 Mechanisms for Real-Time
2.3.2.1 Priority Inheritance Protocol
  The priority inheritance protocol (PIP) makes a low priority task inherit the priority of any higher priority task that becomes blocked on a resource locked by the lower priority task.
  The PIP is not adequate for hard RTSs
2.3.2.2 Priority Ceiling Inheritance Protocol
  The priority ceiling protocol (PCP) associates a ceiling value that is equal to the highest priority of any task that may lock the resource.
  The RTOS scheduler will manipulate task priorities to avoid the problems of PIP.

## Slide 17: 2.3.2 Mechanisms for Real-Time
2.3.2.3 Immediate Ceiling Priority Inheritance Protocol
  The immediate inheritance protocol (IIP) also associates, to each resource, a ceiling value that is equal to the highest priority of any task that may lock the resource. However, different from PCP, in IIP a task is immediately assigned the ceiling priority of the resource it is locking.

## Slide 18: 2.3.3 Commercial RTOSs
The rich set of primitives provided.
  Ex) Tornado/VxWorks, LYNX, OSE, QNX, RT-Linux, and ThreadX
A smaller set of primitives provided.
  Ex) the research RTOS Asterix and the commercial RTOS SSX5
Standard APIs
  Many of the commercial RTOSs provide standard APIs.
  Ex) RT-POSIX, OSEK, APEX

## Slide 19: 2.4 Real-Time Scheduling
Traditionally, real-time schedulers are divided into offline and online schedulers.
  Offline schedulers make all scheduling decisions before the system is executed.
  Online schedulers, on the other hand, decide during execution, based on various parameters, which task should execute at any given time.

## Slide 20: 2.4.1 Introduction to Scheduling
A RTS can be preemptive or nonpreemptive.
  In a preemptive system, tasks can preempt each other, letting the task with the highest priority execute.
  In a nonpreemptive system a task that has been allowed to start will execute until its completion.
Tasks can be categorized into either being periodic, sporadic, or aperiodic.
  Typically, tasks that perform measurements are periodic, collecting some value(s) every nth time unit.
  A sporadic task is typically reacting to an event/interrupt.
  Usually aperiodics are triggered by interrupts.

## Slide 21: 2.4.2 Offline Schedulers
Offline Schedulers (table-driven schedulers)
  The schedulers create a schedule (the table) before the system is started (offline).
  At runtime, a dispatcher follows schedule, and makes sure that tasks are only executing at their predetermined time slots.
  Offline schedules are commonly used to implement the time-triggered execution paradigm.

## Slide 22: 2.4.3 Online Schedulers
Scheduling policies that make their scheduling decisions during runtime are classified as online schedulers.
Schedulers that base their scheduling decisions on task priorities are also called priority-based schedulers.

## Slide 23: 2.4.3.1 Priority-Based Schedulers
Using priority-based schedulers the flexibility is increased, since the schedule is created online.
Fixed-Priority Scheduling (FPS) and Earliest Deadline First (EDF)
  In FPS
    Priorities are assigned to the tasks before execution (offline).
    The task with the highest priority among all tasks that are available for execution is scheduled for execution.
  Using EDF
    The task with the nearest (earliest) deadline among all available task is selected for execution.

## Slide 24: 2.4.3.2 Scheduling with Aperiodics
In order for the priority-based schedulers to cope with aperiodic tasks, different service methods have been presented.
These services are implemented using special server tasks.
  Using FPS, for instance, the Sporadic Server (SS) is presented by Sprunt et al.
  Using EDF, Dynamic Sporadic Server (DSS) extends SS.
  Other EDF-based schedulers are the Constant Bandwidth Server (CBS), presented by Abeni and Buttazzo, and the Total Bandwidth Server (TBS) by Spuri and Buttazzo.

## Slide 25: 2.5 Real-Time Communications
Real-time communication aims at providing timely and deterministic communication of data between distributed devices.
There are real-time communication networks of different types, ranging from small fieldbus-based control systems to large Ethernet/Internet distributed applications.
In this section we give a brief introduction to communications in general and real-time communications in particular.

## Slide 26: 2.5.1 Communication Techniques
CSMA/CD (Carrier Sense Multiple Access/ Collision Detection)
  CSMA/CD is used, for example, in Ethernet.
CSMA/CA (Carrier Sense Multiple Access/ Collision Avoidance)
  Examples of networks that implement CSMA/CA are Controller Area Networks (CAN) and ARINC 629
TDMA
  One example of a TDMA-based real-time network is TTP.
Tokens
  Tokens are used in, for example, Profibus.
Mini slotting
  Mini slotting can be found in, for example, FlexRay and ARINC 629

## Slide 27: 2.5.2 Fieldbuses
Fieldbuses are a family of factory communication networks that have evolved as a response to the demand to reduce cabling costs in factory automation systems.
  Fieldbuses used in the automotive industry are, for example, CAN, TT-CAN, TTP, LIN, and FlexRay.
  In avionics, ARINC is one of the frequently used communication standard.
  Profibus is widely used in automation and robotics.
  In trains TCN and WorldFIP are very popular communication technologies.

## Slide 28: 2.5.2 Fieldbuses
2.5.2.1 Controller Area Network
  The Controller Area Network (CAN) was standardized by the International Standardisation Organisation (ISO) in 1993.
    Today CAN is a widely used fieldbus.
    CAN is an event-triggered broadcast bus designed to operate at speeds of up to 1 Mbps.
    CAN is using a fixed-priority based arbitration mechanism.
    CAN is a collision-avoidance broadcast bus. (so-called CSMA/CA)

## Slide 29: 2.5.2 Fieldbuses
2.5.2.2 Time-Triggered CAN
  Time-triggered communication on CAN (TT-CAN) is a standardized session layer extension to the original CAN.
    In TT-CAN, the exchange of message is controlled by the temporal progression of time, and all nodes are following a predefined static schedule.
    It is also possible to support original event-triggered CAN traffic together with the time-triggered traffic.
    The static schedule is based on a time division (TDMA).
    Several semiconductor vendors are manufacturing TT-CAN compliant devices.

## Slide 30: 2.5.2 Fieldbuses
2.5.2.3 Flexible Time-Triggered CAN
  Flexible time-triggered communication on CAN (FTT-CAN) provides a way to schedule CAN in a time-triggered fashion with support for event-triggered traffic as well.
    FTT-CAN supports both periodic and aperiodic traffic by dividing the EC into two part.
    FTT-CAN is still mainly an academic communication protocol.

## Slide 31: 2.5.2 Fieldbuses
2.5.2.4 Time-Triggered Protocol
  The Time-Triggered Protocol Class C (TTP/C) is a a TDMA based communication network intended for truly hard real-time communication.
    TTP/C is available for network speeds of up to 25Mbps.
    TTP/C is part of the Time-Triggered Architecture (TTA) by Kopetz, which is designed for safety critical applications.
    TTP/C has support for fault tolerance, clock synchronization, membership services, fast error detection, and consistency checks.
    For the less hard RTSs, there exists a scaled-down version of TTP/C called TTP/A.

## Slide 32: 2.5.2 Fieldbuses
2.5.2.5 Local Interconnect Network
  The Local Interconnect Network LIN, was developed by the LIN Consortium as a low cost alternative for small networks.
    LIN is cheaper than, for example, CAN.
    LIN is using the UART/SCI interface hardware, and transmission speeds are possible up to 20 Kbps.
    The traffic is sent in a time-triggered fashion.
2.5.2.6 FlexRay
  FlexRay was proposed in 1999 by several major automotive manufacturers, for example, Daimler-Chrysler and BMW, as a competitive next generation fieldbus replacing CAN.

## Slide 33: 2.5.2 Fieldbuses
2.5.2.6 ARINC 629
  For avionic and aerospace communication systems, the ARINC 429 standard and its newer ARINC 629 successor are the most commonly used communication systems today.
    ARINC 629 supports both periodic and sporadic communication.
    The bus is scheduled in bus cycles, which in turn are divided in two parts.
    The arbitration of message is based on collision avoidance using mini-slotting.
    Network speeds as high as 2Mbps

## Slide 34: 2.5.2 Fieldbuses
2.5.2.8 Profibus
  Profibus is used in process automation and robotics.
  There are three different version of Profibus:
    Profibus-DP, Profibus-PA, Profibus-FMS
  Profibus is available with data rates up to 12Mbps.
2.5.2.9 Train Communication Network
  The Train Communication Network (TCN) is widely used in trains, and implements the IEC 61275 standard as well as the IEEE 1473 standard.
    TCN is composed of two networks:
      The Wire Train Bus (WTB) and the Multifunction Vehicle Bus (MVB).
      The WTB’s network data rate is up to 1 Mbps.
      The MVB’s data rate is 1.5 Mbps.

## Slide 35: 2.5.2 Fieldbuses
2.5.2.10 WorldFIP
  The WorldFIP is a very popular communication network in train control systems.
    WorldFIP is based on the Producer-Distributor-Consumers (PDC) communication model.
    Currently, network speeds are as high as 5Mbps.
    The WorldFIP protocol defines an application layer that includes PDC- and messaging-services.

## Slide 36: 2.5.3 Ethernet for Real-Time Communincation
Ethernet is not originally developed for real-time communication since the original intention with Ethernet is to maximaze throughput (bandwidth).
However, nowadays, a big effort is being made in order to provide real-time communication using Ethernet.

## Slide 37: 2.5.3 Ethernet for Real-Time Communincation
2.5.3.1 TDMA
  A simple solution would be to eliminate the occurrence of collisions on the network.
  This has been explored by, for example, Kopetz et al., using a TDMA protocol on top of Ethernet.
2.5.3.2 Usage of Tokens
  Another solution to eliminate the occurrence of collisions is the usage of tokens.
  Token-based solutions on the Ethernet also eliminates collisions, but is not compatible with standard hardware.

## Slide 38: 2.5.3 Ethernet for Real-Time Communincation
2.5.3.3 Modified Collision Resolution Algorithm
  Using standard Ethernet controllers, the modified collision resolution algorithm is nondeterministic.
  In order to make a deterministic modified collision resolution algorithm, a mojor modification of the Ethernet controllers is required
2.5.3.4 Virtual Time and Window Protocols

## Slide 39: 2.5.3 Ethernet for Real-Time Communincation
2.5.3.5 Master/Slave
  As a part of the FTT framework, FTT Ethernet is proposed as a master/multislave protocol.
2.5.3.6 Traffic Smoothing
  Traffic smoothing can be used to eliminate bursts of traffic that have severe impact on the timely delivery of message packets on the Ethernet.
  Traffic smoothing could be a solution for soft RTSs.

## Slide 40: 2.5.3 Ethernet for Real-Time Communincation
2.5.3.7 Black Bursts
  Black burst is implementing a collision avoidance protocol on Ethernet.
  When a station want to submit a message, the station waits until the network is idle, no traffic is being transmitted.
2.5.3.8 Switches
  By using these switches, a collision free network is provided.
  However, this requires new hardware supporting the IEEE 802.1p standard.

## Slide 41: 2.5.4 Wireless Communication
There are no commercially available wireless communication protocols providing real-time guarantees.
Today, a big effort is being made (as with Ethernet) to provide real-time guarantees for wireless communication, possibly by using ether WLAN or Bluetooth.