## Slide 1: TTP – A Time-Triggered Protocol for Fault-Tolerant Real-Time System Author : H. Kopetz and G. Grunsteidl
Real-Time Computing and Communications Lab.
Hanyang University
Heejin Kim
2006.11.6

## Slide 2: Contents
Introduction
Architectural characteristics
Protocol objectives
Design rationale
Protocol description
Protocol characteristics
Conclusion

## Slide 3: Introduction
Event-triggered (ET) architectures
  All activities are initiated as a consequence of the occurrence of event.
Time-triggered (TT) architectures
  They are driven by the progression of global time.
TT Architectures are less flexible but are easier to analyze and to test than ET Architectures
The Time-Triggered Protocol is an integrated communication protocol for time-triggered architectures

## Slide 4: Architectural characteristics (1/3)
System structure
  To tolerate the failure of a node, nodes can be replicated also and grouped into Fault Tolerant Units (FTUs)
  Every node possesses a communication controller with two bidirectional communication ports, connected to the two replicated broadcast channels

## Slide 5: Architectural characteristics (2/3)
Fault hypothesis and system configuration
  We assume that node failures are of the fail-silent type and channel failures are omission failures Omission failure : A server omits to respond to a request Fail-Silence : A subsystem is fail-silent if it either produces correct results or no results at all, i.e., it is quiet in case it cannot deliver the correct service

## Slide 6: Architectural characteristics (3/3)
System configurations
Class Ⅰ One node/FTU, 2 frames/FTU
Class Ⅱ Two active nodes/FTU, 2 frames/FTU
Class Ⅲ Two active nodes/FTU 4 frames/FTU
Class Ⅳ Two active nodes One shadow node/FTU 4 frames/FTU

## Slide 7: Protocol objectives
Message transport with predictable low latency
Fault tolerance
Temporary blackout handling
Clock synchronization
Membership service
Distributed redundancy management
Support for rapid mode change
Minimal overhead
Utmost flexibility without compromising predictability

## Slide 8: Design rationale
Sparse time Base
  The occurrence of significant events is restricted to the lattice points of a globally synchronized action lattice
Use of apriori Knowledge
  In a time-triggered architecture much information about the behavior of the system is known a priori to all nodes of the ensemble
State agreement
  A receiver can only interpret the frame sent by a sender if sender and receiver agree about the controller state at the time of sending and receiving
Fail silence
  TTP is based on the assumption that the communication channels have only omission failures and the nodes support the fail-silent abstraction
Design tradeoffs
  In TTP the design tradeoff between processing requirements at the nodes and bandwidth requirements of the channel

## Slide 9: Protocol description (1/9)
Controller state ( C-state)
  mode field
    The mode field contains a systemwide unique identification of the current operational mode
  time field
    The time field denotes current global time
  membership field
    The membership field indicates which FTU has been active and which FTU has been inactive at its last membership point

## Slide 10: Protocol description (2/9)
Frame format
  Start of frame(SOF)
    The SOF identifies the beginning of a new frame
  Control field
    The control field has three subfields
      Initialization bit (I/N), Mode change field, Acknowledgment field
  Data field
    The data field consists of the concatenation of one or more messages containing application data
  Cyclic redundancy check (CRC)
    The CRC has a length of two bytes
  Interframe delimiter(IFD)
    The IFD is required for the proper bit synchronization of sender and receiver

## Slide 11: Protocol description (3/9)
  Typical frame format

## Slide 12: Protocol description (4/9)
CRC calculation
  The CRC calculation is different for Initialization frames (I-frames) and normal frames (N-frames).
  For I-frames the CRC field is calculated over the control field concatenated with the data field of the frame
  For N-frames the CRC field is calculated over the C-state of the controller concatenated with the control field and the data field of the frame

## Slide 13: Protocol description (5/9)
Clock synchronization
  TTP provides the fault-tolerant internal synchronization of the local clocks to generate a global time-base of known precision
  Continuous clock synchronization is performed without any overhead in frame length or frame number by applying the fault-tolerant average algorithm periodically, preferably with hardware support

## Slide 14: Protocol description (6/9)
Bus access
  Bus access is controlled by the global time
Membership service
  The membership service records which FTU is active and which FTU is inactive at membership points of the nodes
  When an FTU has the right to transmit, it sets its own membership flag in the current membership field to one

## Slide 15: Protocol description (7/9)
Mode change
  At any point in time, the ensemble of FTUs operates in a particular operating mode
  If a FTU intends to change this operating mode, it alerts all other nodes about this mode change by specifying the successor mode in the mode subfield of the control field at its next membership point
  Mode changes are well-suited to react to sporadic events that require immediate service from the whole ensemble of FTUs

## Slide 16: Protocol description (8/9)
Redundancy management and initialization

## Slide 17: Protocol description (9/9)
Temporary blackout handling
  Blackout detection
    Rapid blackout detection is performed by continuous monitoring of the membership field
  Blackout monitoring
    Monitor the membership to see if some other nodes start to recover
  Blackout recovery
    After the membership has stabilized a mode change to a global emergency service mode will be activated

## Slide 18: Protocol characteristics (1/3)
Temporal encapsulation of the nodes
  This temporal encapsulation leads to significant improvements in the fields of testability, system simulation and determinism
Flexibility
  Extensibility
    The TDMA sequence and the data formats of TTP are controlled by the mode definition
    TTP allows the design of decomposable systems
  Compatibility
    TTP has a predictable response time and an unrestricted length of the data field
  Flexible redundancy
    TTP supports different redundant configuration classes

## Slide 19: Protocol characteristics (2/3)
Performance comparison

## Slide 20: Protocol characteristics (3/3)
Implementation considerations
  Signaling method
    No restrictions on the signaling method employed
  Host interface
    Dual-ported RAM
  VLSI implementation

## Slide 21: Conclusions
Distributed real-time control systems must support fault tolerance and must have a guaranteed response time
TTP provides all service that are needed for the implementation of a fault-tolerant real-time system with guaranteed timeliness