## Slide 1: Module 12 Communication-Centric SoC Platform Architecture
조준동 교수
(성균관대학교)

## Slide 2: 목차
Introduction
AMBA
Coreconnect
WISHBONE
Sonics µNetworks
Open Core Protocol
PI-Bus
CoreFrame
참고 문헌

## Slide 3: Introduction 1
System-On-Chip 설계에서 이미 설계된 코어들을 연결시켜 시스템을 구성하기 위해 가장 필요한 기술 중에 하나는 on chip bus 기술이다.
Bus란 Processor와 다른 device (input/output device, memory 등)를 연결하는 communication channel을 의미한다.
Bus의 기본 3요소
  address bus
  data bus
  control bus
Notes: 1. 성능의 극대화를 위해 기존의 PCB 상에서 사용되던 버스대신에 별도의 온칩 버스들이 제안되고 있으며, 시스템 통합을 빠르고 용이하게 하기 위해서, 버스 자체에 대한 표준화가 이루어 지고 있으며, 표준화를 위한 많은 연구와 모임들이 진행되고 있다.
2. 물리적으로는 wire로 이루어져 있으며 논리적인 의미에서는 master와 slave사이에 signal(또는 data) 전송에 대한 protocol을 의미한다. Master란 일반적으로 Processor를 의미하며, 이는 bus의 사용에 주도적인 역할을 하는 장치이다. Slave는 master의 반대적인 입장이 된다. Bus의 모든 동작은 master가 주체가 되어 기술된다..
3. Address bus는 master가 요청하는 data가 존재하는 address를 전송하는 line이며, data bus 는 실제 data가 전송되는 line이다. Control bus는 data 전송에 관련된 control signal을 전송하는 line이다. Address와 control bus는 master에서 slave로만 전송되는 단방향이지만, data bus는 read와 write를 동시에 해야 하기 때문에 양방향이거나 read data와 write data bus를 양분해 놓는다.

## Slide 4: Blocking/Non-Blocking Communication
We distinguish between blocking and non-blocking
communication:
blocking communication: the process element
initiating the communication goes in a waiting state
until communication end.
non-blocking communication: the process element
initiating the communication can execute other
useful tasks during an ongoing communication.
both types of communication are useful.

## Slide 5: Two major communications
shared memory
message passing
Notes: need of atomic „test-and-set“ operations, else:
􀂊 PE 1 reads flag location and sees „not busy“
􀂊 PE2 reads flag location and sees „no busy“
􀂊 PE1 sets flag location to „busy writing“ and writes data
to the shared location
􀂊 PE2 erroneously sets flag „busy writing“ and overwrites
the data left by PE1
􀂊 a semaphore is a language level synchronization
element
􀂊 with semaphores guarded access to shared memory
can be realized:
􀂊 wait for semaphore: P();
􀂊 P() uses a test-and-set operation to repeatedly test a
location that holds a memory lock
􀂊 release semaphore: V();
􀂊 V() resets the memory lock
Message Passing Communication
each communication entity has its own send/receive
unit
􀂊 message is stored on endpoints of send/receive
unit and not in communication link as at shared
memory communication
􀂊 message passing is used at applications where units
operate relatively autonomous: ex. car control
system
PE1 PE2
send/receive send/receive
message

## Slide 6: Predefined master/slave devices
device 1 is master and initiates communication
device 2 is slave
send or receive is possible
data bus is bidirectional

## Slide 8: Shared communication channel (Shared bus)
Notes: 현재 사용되는 거의 모든 bus는 shared communication channel로 구성되며, 이는 여러 개의 master와 slave가 하나의 bus를 이용하여 communication을 한다는 의미이다
여러 개의 master와 slave가 하나의 bus를 이용하여 communication을 한다는 의미이다. 여러 개의 master의 bus 사용을 중재하기 위하여 “arbiter”가 필요하다.
master는 bus를 사용하기 위해서 arbiter에 request를 하고, arbiter는 다른 master가 bus를 사용하고 있지 않으면 해당 master에게 bus 사용 허가를 나타내는 grant를 부여하게 된다.

## Slide 9: Typical Processor Bus
a bus is a collection of wires as well as a protocol
microprocessor buses build on handshake protocol
basic bus operations are reading and writing
system clock helps to increase data transfer speed

## Slide 10: Bus With DMA Controller
DMAcontrollers perform direct data transfers between devices without CPU involvement
four-cycle-handshake with processor to get bus
master (interrupt processor when finished)
used for high speed requirements
to prevent to block the processor too long, partial
block transfer mode possible, 16, 32 or 256 words
bus DMA controller is a bus with 2 masters

## Slide 11: Bus bridge: slave at fast bus, master at slow bus
high-speed buses provide wider data connections
high-speed buses require more expensive circuitry and connectors. The cost of low-speed devices can be held down by using lower-speed, lower-cost bus.
The bridge may allow the buses to operate independently, thereby providing some parallelism in processing an I/O operations.

## Slide 12: Standard SoC Bus
􀂊 Avalon from Altera Inc., used for Nios
􀂊 AMBATM bus from AMD Inc., used for ARM
􀂊 CoreConnectTM from IBM Inc., used for PowerPC
  Creating an SoC is easier.
    Cores already ‘speak’ the same language
  Improves reusability of IP cores
    More usage means lesser bugs
  Improves portability
    Between languages
    Between technologies
  Improves reliability
    Lesser bugs
    Less error prone handlings (wrappers, bridges, etc)

## Slide 13: Bus architecture type
  Common memory-I/O bus
  Independent I/O bus
Notes: common memory-I/O bus : memory와 I/O device가 같은 bus를 사용
independent I/O bus : memory와 I/O device가 서로 다른 bus를 사용
그림2는 independent I/O bus의 구조를 보여준다. Memory와 연결된 bus를 system bus라고 하며, I/O device와 연결된 bus를 peripheral bus라고 한다.
System bus와 peripheral bus는 bridge를 통하여 연결된다.

## Slide 14: AMBA (Advanced Microcontroller Bus Architecture)
The advanced high-performance bus (AHB)
􀂊 high-performance
􀂊 pipelined operation
􀂊 multiple bus master
􀂊 burst transfer
􀂊 split transactions
The Advanced System Bus (ASB)
  dito, but no split transactions
The Advanced Peripheral Bus (APB)
  􀂊 low-power
  􀂊 latched address and control
  􀂊 simple interface
  􀂊 suitable for many peripherals
AMBA는 embedded microcontroller의 설계를 위한 on-chip communication의 표준안이 되고 있다.
Notes: AHB : high-performance,high-clock-frequency system modules.
ASB : high-performance system modules. where the high-performance features of AHB are not required. ( 잘 사용하지 않음)
APB : optimised for minimal power consumption and reduced interface complexity to support peripheral functions

## Slide 15: AMBA
A typical AMBA-based microcontroller
Notes: AMBA-based microcontroller는 일반적으로 AHB나 ASB를 backbone bus로 사용한다. 여기에는 ARM과 같은 CPU나 DMA (Direct Memory Access)등이 연결될 수 있다.
또한 peripheral macrocell communication을 위해서 APB가 붙을 수 있는데 이것은 ASB나 AHB의 local bus처럼 여겨지며 Bridge를 사용하여 연결된다.

## Slide 16: AMBA
Bus Interconnection
Notes: AMBA의 design에는 Multiplexer, arbiter, decoder가 있어 여러 개의 Master와 Slave를 중개해 주는 역할을 한다.

## Slide 17: AMBA Signals
H : AHB signal임을 의미한다
B : ASB signal임을 의미한다
A : ASB의 arbiter와 master간에 사용되는 signal임을 의미한다
D : ASB의 decoder에 사용되는 signal임을 의미한다.
P : APB signal임을 의미한다.
예를 들어서 HREADY라 함은 AHB의 HIGH에서 동작하는 signal임을 의미하고, BnRES라 함은 ASB의 LOW에서 동작하는 reset signal임을 알 수 있다.
Notes: AMBA의 signal들에는 항상 첫 글자에 특정한 letter가 사용된다. 또한 n이라는 문자가 사용되는 것은 active LOW라는 의미를 가지고 있다. 그 이외의 signal들은 모두 대문자로 표현되며 active HIGH의 의미를 갖는다.

## Slide 18: AMBA AHB signal list
신호명 | Source |  | 설명
HCLK | clock | AHB | bus clock, 모든 bus transfer의 timing, realted to the rising edge of HCLK
HRESETn | reset | // | reset system and bus, active LOW
HADDR[31:0] | master | // | 32bit address bus
HTRANS[31:0] | // | // | transfer type, NONSEQ/SEQ/IDLE/BUSY
HWRITE | // | // | transfer 방향, HIGH : write transfer, LOW : read transfer
HSIZE[2:0] | // | // | transfer 크기, byte/half-word/word
HBURST[2:0] | // | // | burst type, burst의 일부분 여부를 알려줌. 4/8/16bit burst
HPROT[3:0] | // | // | protection control, opcode fetch/data access, privileged/user mode access.
HWDATA[31:0] | // | // | write data bus(32bit), data를 write operation 동안 master에서 slave로 전달
HSELx | decoder | // | slave sel, 각 slave의 선택신호, 간단히 address bus의 combinational decode

## Slide 19
HRDATA[31:0] | slave | // | read data bus, data를 read operation 동안 slave에서 master로 전달
HREADY | // | // | transfer done, HIGH : bus에서 transfer 완료. ※bus의 slave는 신호 입출력에 이 신호를 요구한다.
HRESP[1:0] | // | // | transfer response, 전달 상태 정보. OKAY/ERROR/RETRY/SPLIT
HBUSREQx | master | Arbi- trate | bus request, master x가 bus를 요구한다고 arbiter에 보내는 신호, 최대 16개
HLOCKx | // | // | locked transfer, HIGH : master가 locked access를 요구, 다른 master는 bus를 사용할 수 없다
HGRANTx | arbiter | // | bus grant, master x가 현재 priority mater임. address/control 신호의 소유는 전송의 끝에서 HREADY가 HIGH이면 바뀌게 된다. 따라서 한 master는 (HREADYandHRANTx=1)일 때 access할 수 있다.
HMASTER[3:0] | // | // | master number, arbiter로부터의 현재 전송을 하고 있는 master의 정보
HMASTERLOCK | // | // | 현 master가 locked 전송 sequence라는 것을 알려주는 신호
HSPLITx[15:0] | slave | // | split completion request, 어떤 bus master가 split 전송을 재시도하기 위해 사용되어야 하는지를 slave에서 arbiter로 전달(16)

## Slide 20
신호명 | 비고 | 설명
PCLK | APB | bus clock, APB의 timing, rising-edge
PRESETn | // | system bus reset에 직접 연결되는 bus reser, active LOW
PADDR[31:0] | // | APB address bus, peripheral bus bridge에 의해 drive되는 32bit address
PSELx | // | peripheral bus bridge unit내의 두 번째 decoder로부터 각 peripheral bus slave x에 전달되는 신호, 이 신호는 slave가 선택되고, data 전달이 요구된다는 것을 의미한다.
PENABLE | // | APB strobe, peripheral bus 상의 timing을 strobe. APB 전송의 두 번째 cycle을 알려준다.
PWRITE | // | APB 전송 방향, HIGH : APB write access, LOW : read access
PRDATA | // | APB read data bus, read cycle동안 선택된 slave에 의해 drive된다.(PWRITE : LOW시)
PWDATA | // | write data bus, write cycle동안 peripheral bus bridge unit에 의해 drive된다.(PWRITE : HIGH)

## Slide 21: Advanced High-Performance Bus (AHB)
􀂊 AHB master:
  􀂊 able to initiate read and write transfers
  􀂊 only one bus master is allowed to control the bus
􀂊 AHB slave:
  􀂊 responds to read and write operations in a given address
  space
  􀂊 signals back to the master: success, failure or waiting of
  the data transfer
􀂊 AHB arbiter:
  􀂊 ensures that only one master at a time is allowed to
  control bus
  􀂊 any arbitration algorithm can be used, like highest
  priority, fair access, etc
􀂊 AHB decoder:
  􀂊 decodes address and generates device select signals
  􀂊 single centralized decoder is required

## Slide 22: AMBA
AMBA AHB system을 구성하는 요소는 다음과 같다.
구성 요소 | 설 명
AHB Master | Bus Master는 Address나 control signal들을 내보냄으로 read나 write의 operation을 할 수 있도록 해 주는 장치이다. 한번에 하나의 Master만이 전송을 가능하게 한다
AHB Slave | Bus Slave는 주어진 address-space안에서 read와 write를 가능하게 해주는 장치이다. Slave는 ready등의 signal을 통해서 master로 하여금 기다리게 하거나 전송이 잘 못되었음을 알린다
AHB arbiter | Bus Arbiter는 한번에 오직 하나의 Master가 선택되도록 하는 역할을 한다. 고유의 priority algorithm을 가지고 이러한 arbitration을 하게 되는데, AHB에는 오직 하나의 arbiter가 존재하게 된다.
AHB decoder | AHB decoder의 역할은 Master로 나오는 Address의 상위 비트를 가지고서 적절한 slave를 선택해 주는 것이다. AHB에는 역시 하나의 Decoder가 존재한다
Notes: AMBA AHB에는 하나 또는 그 이상의 bus master가 연결된다. 이러한 것들에는 DMA나 DSP같은 것들이 연결 될 수 있다.
External memory interface나 APB bridge등은 AMBA AHB의 slave로 연결 될 수 있다. 그러나 low-bandwidth를 갖는 peripheral 장치들은 APB를 통해서 연결이 되어야 할 것이다.

## Slide 23: AMBA AHB Interconnection Schema
  arbiter determines bus master
  central multiplexor schema
  central decoder for read data
  additional characteristics:
    single cycle bus master handover
    single clock edge operation
    non-tristate implementation
    wider data bus configuration (64/128 bits)
Notes: Non-tristate implementation => write data(WDATA)와 read data(RDATA)가 분리되어 있음.
AMBA AHB에는 하나 또는 그 이상의 bus master가 연결된다. Master에는 DMA나 DSP같은 것들이 연결 될 수 있다. External memory interface나 APB bridge등은 AMBA AHB의 slave로 연결 될 수 있다. 그러나 low-bandwidth를 갖는 peripheral 장치들은 APB를 통해서 연결된다.

## Slide 24: Basic AHB Transfer
Phases:
  address & control phase
  one or more data phase
Slave can delay transfer with HREADY
address source is master: HADDR[31:0]
data source for write operations is master: HWDATA[31:0]
data source for read operations is slave: HRDATA[31:0]
Notes: AHB의 transfer에는 2가지 중요한 사실이 있다.
Address phase에 있어서 오직 single cycle만으로 구성된다.
Data phase에서는 HREADY signal을 사용하여 몇 cycle동안의 데이터의 extend가 가능하다.
Master는 항상 HCLK의 rising edge에서 address와 control signal을 전송하게 된다. 그 다음의 rising edge에서 slave는 address와 control signal을 sampling하게 되고 그 다음의 rising edge에서 해당 data를 받는다.

## Slide 25: AHB Transfer Example
Master shows transfer type with HTRANS[1:0]
  IDLE (“00“): no data transfer is required
  BUSY (“01“): master is delaying an ongoing transfer
  NONSEQUENTIAL (“10“): first transfer of a burst or
  single transfer
  SEQ (“11“): remaining transfers of a burst
􀂊 Delaying transfer
  􀂊 master delays transfer with HTRANS[1:0]
  􀂊 slave delays transfer with HREADY
􀂊 incremental burst of unspecified length is shown

## Slide 26: AHB Transfer Example (4-beat wrapping burst)
Master defines bus operation with HBURST[2:0]
  􀂊 SINGLE (“000“): single transfer
  􀂊 INCR (“001“): increment burst of unspecified length
  􀂊 WRAP4 (“010“): 4-beat wrapping burst
  􀂊 INCR4 (“011“): 4-beat incrementing burst
  􀂊 WRAP8 (“100“): 8-beat wrapping burst
  􀂊 INCR8 (“101“): 8-beat incrementing burst
  􀂊 WRAP16 (“110“): 16-beat wrapping burst
  􀂊 INCR16 (“111“): 16-beat incrementing burst
Burst must not cross 1kB address boundary

## Slide 27: AHB Transfer Example with Response
slave can complete a transfer in a number of ways:
  􀂊 complete the transfer immediately
  􀂊 insert wait states
  􀂊 signal an error to indicate transfer has failed
  􀂊 delay the completion of the transfer, but allow
  master/slave to back off bus
slave shows status of transfer with HRESP[1:0] in
combination with HREADY
  􀂊 OKAY: transfer is progressing normally
  􀂊 ERROR: transfer has been unsuccessful
  􀂊 RETRY and SPLIT: both indicate that transfer cannot
  complete immediately
􀂊 ERROR, RETRY and SPLIT are at least two-cycles

## Slide 29: AHB Transfer type
HTRAN [1:0] | Type | Description
00 | IDLE | 아무런 전송이 필요하지 않음을 의미한다. 즉 해당 master에게 grant가 이루어 졌지만 아무런 전송을 하지 않으려 할 때에 IDLE transfer를 하게 된다. Slave는 zero wait state의 OKAY response를 하며 transfer는 slave에 의해서 무시 되어진다.
01 | BUSY | BUSY transfer는 burst transfer의 중간에 IDLE cycle을 넣으려고 할 때 나타난다. 즉 master가 계속하여 burst transfer를 하려고 하지만 즉시 다음 전송이 이루어 질 수 없는 상황에서 BUSY을 나타낸다. BUSY의 cycle에서는 현재의 모든 control signal들이 다음 cycle로 전달되며 BUSY 상태의 전송은 slave에 의해서 모두 무시 되어야 한다. Slave는 IDLE 상태와 같이 zero wait state의 OKAY response를 해야 한다.
10 | NON SEQ | Burst transfer의 첫번째 전송을 의미하거나 single transfer를 의미한다. 또한 현재 Address와 control signal들은 전의 transfer와 상관이 없음을 알려준다.
11 | SEQ | Burst transfer의 나머지는 모두 SEQUENTIAL로 나타나며 이것은 전의 address와 control이 현재의 transfer와 상관이 있다는 것을 알려준다. 그리하여 현재의 address는 전의 address에서 transfer size 만큼이 더해져서 나타나게 된다.

## Slide 30: Burst operation
HBURST[2:0] | Type | Description
000 | SINGLE | Single transfer
001 | INCR | Incrementing burst of unspecified length
010 | WRAP4 | 4-beat wrapping burst
011 | INCR4 | 4-beat incrementing burst
100 | WRAP8 | 8-beat wrapping burst
101 | INCR8 | 8-beat incrementing burst
110 | WRAP16 | 16-beat wrapping burst
111 | INCR16 | 16-beat incrementing burst
Notes: 4, 8, 또는 16개의 burst transfer가 AMBA AHB protocol에서 정의 된다. 또한 1개의 전송도 가능하며, incrementing이나 wrapping burst mode가 지원된다.
Incrementing burst는 address가 순차적으로 burst size에 따라서 커지는 것을 의미한다. 그러므로 다음의 address는 전의 address에서 size만큼 더해 주면 된다.
Wrapping burst에서는 size*beat 만큼의 address boundary가 설정이 된다. 그러므로 Address가 incrementing burst와 같이 증가하다가 boundary에 이르면 다시 밑의 boundary에서 시작하게 된다.
Bursts는 1kB의 address boundary를 넘지 못한다. 그러므로 master가 fixed length로 incrementing burst를 할 때 boundary를 넘지 않도록 하는 것은 중요하다.
Incrementing burst는 어떠한 길이의 transfer라도 1kB의 boundary를 넘지 않는 선에서 얼마든지 가능하다.
burst type외에도 transfer를 이루기 위해서 몇 가지 control signal들이 사용된다. Transfer의 방향을 설정해 주는 HWRITE와 transfer size를 알려주는 HSIZE[1:0]과 protection control을 위해서 사용되는 HPROT[3:0]이 그것이다.

## Slide 31: Transfer direction & size
HWRITE가 HIGH일 때, 이 signal은 HWDATA[31:0]을 사용하여 write하는 과정임을 알려준다. HWRITE가 LOW일 때는 HRDATA[31:0]을 사용하여 read하는 과정임을 알려준다.
HSIZE[2:0] | Size | Description
000 | 8 bits | Byte
001 | 16 bits | Half word
010 | 32 bits | Word
011 | 64 bits | 
100 | 128 bits | 4-word line
101 | 256 bits | 8-word line
110 | 512 bits | 
111 | 1024 bits | 

## Slide 32: Protection control
HPROT[3:0]은 opcode fetch인지 data access인지 또는 privileged mode access인지 user mode인지 등을 알려주기 위한 것이다
HPROT[3] cacheable | HPROT[2] bufferable | HPROT[1] privileged | HPROT[0] Data/opcode | Description
- | - | - | 0 | Opcode fetch
- | - | - | 1 | Data access
- | - | 0 | - | User access
- | - | 1 | - | Privileged access
- | 0 | - | - | Not bufferable
- | 1 | - | - | Bufferable
0 | - | - | - | Not cacheable
1 | - | - | - | cacheable
Notes: 그러나 이러한 protection mode에도 불구하고 HPROT의 사용을 하지 않는 것을 권장한다. 그러므로 slave는 HPROT의 정보를 사용할 필요는 없다.

## Slide 33: Address decoding
각각의 slave에 붙어있는 HSELx의 signal을 enable해주기 위한 장치
Select signal은 high-order address signals을 사용하여 구현된다.
slave는 HREADY가 HIGH일 때에만 HSELx의 signal을 바꾸어야 한다는 것이다. 경우에 따라서는 HREADY가 LOW일 때 HSELx signal을 바꾸어도 되지만 이 경우에는 Slave쪽에서 마지막 전송이 끝날 때에만 선택되는 slave가 바뀌어야 한다.
하나의 slave가 가질 수 있는 address의 boundary는 1kB이다. Bus master는 1kB의 boundary를 넘어서 burst를 할 수 없도록 design되어 있기 때문에 이러한 설정이 가능하다. 이 경우에도 default slave가 있어야 하는데 master가 잘못된 영역의 address에 쓰려고 하는 경우에 이 default slave가 선택이 되어야 하며 선택된 slave는 SEQUENTIAL이나 NONSEQUENTIAL일 경우에는 ERROR response를 IDLE이나 BUSY일 경우에는 OKAY response를 내보내 주어야 한다.
Notes: 􀂊 slaves sample HSELx when HREADY is active
􀂊 minimum address space allocated to a slave is 1kB
􀂊 if system does not contain complete memory map,
default slave (decoder) should respond to wrong
addresses
􀂊 access attempt to nonexistent location will be
answered by default slave:
􀂊 ERROR response to NONSEQUENTIAL or SEQUENTIAL
􀂊 zero wait state OKAY response to IDLE or BUSY
􀂊 Master determines transfer size with HSIZE[2:0]
􀂊 “000“: size is byte
􀂊 “001“: size is half-word
􀂊 “010“: size is word
􀂊 ...
􀂊 “111“: size is 32 bytes

## Slide 35: Slave select signals
Arbiter

## Slide 36: Slave transfer responses
Transfer done : HREADY를 통해서 AHB는 transfer를 extend시키거나 끝을 알릴 수 있다. 그러나 extend되는 것에는 미리 예측 할 수 있는 Maximum이 있어서 그 이상을 넘어가면서 HREADY를 LOW로 지속 할 수는 없다. 권장되는 maximum wait states는 16이다.
Transfer response :HREADY가 HIGH일 때와 OKAY response는 transfer가 정상적으로 이루어 졌음을 의미한다. 그리고 ERROR response는 ROM에다 쓰려고 하는 등 잘못된 address에 데이터를 access하려고 할 때 나타난다. SPLIT과 RETRY는 transfer를 delay하기 위한 것이다.
HRESP[1:0] | Type | Description
00 | OKAY | OKAY response와 HREADY가 HIGH이면 정상적으로 전송이 이루어 졌음을 의미한다. 또한 OKAY를 통하여 추가적인 cycle을 삽입하기 위하여 사용되기도 한다.
01 | ERROR | Master에게 transfer가 Error가 발생하였고 더 이상 같은 영역에transfer를 계속 할 수 없음을 알린다. Error condition을 위해서 2-cycle이 필요하다.
10 | RETRY | Transfer가 아직 성공적으로 끝나지 않았음을 알리고 transfer를 다시 할 것을 알리는 response이다. Retry condition을 위해서 2-cycle이 필요하다.
11 | SPLIT | Transfer가 아직 성공적으로 끝나지 않았음을 알리고 다른 transfer를 원하는 master에게 그 소유권을 넘겨주기 위한 response이다. Split condition을 위해서 2-cycle이 필요하다.
Notes: 일단 master가 transfer를 시작하면 slave는 이 transfer가 어떻게 진행되어야 할지를 결정해 주어야 한다. Slave가 선택이 되어지면 slave는 HREADY와 HRESP[1:0]을 통하여 transfer에 대한 response를 하게 된다

## Slide 37: AHB Bus Arbitration
Master가 Bus에 대한 Access를 얻는가를 설정
Master는 REQUEST/GRANT interface를 가지고 있어야 하며, Arbiter에게 Request를 했을 때, Arbiter는 고유의 Priority scheme을 가지고, 어떤 Master가 가장 높은 Priority를 갖는 가를 계산해서 그 해당 Master에게 Grant Signal을 보낸다.
또한 각각의 Master는 HLOCKx signal을 갖는데 이것은 Master가 bus의 독점적인 access를 하려고 할 때 발생된다. 즉 현재 Grant된 Master의 LOCK이 enable상태일 때에는 다른 Priority가 높은 Master가 Bus를 요구했을지라도 현재의 Master의 전송이 끝날 때 까지는 Bus를 넘겨주지 않는다.
Notes: signals for bus arbitration:
􀂊 HBUSREQx: master sends bus request
􀂊 HGRANTx: arbiter issues bus grant
􀂊 HMASTER[3:0]: arbiter issues bus master number
􀂊 HLOCKx: master may request bus lock
􀂊 HMASTLOCKx: arbiter issues bus lock grant signal
􀂊 arbiter can terminate non size-limited bursts early
􀂊 master can require locked access
􀂊 if a master looses bus access in the middle of a burst
it must re-assert HBUSREQx to regain access

## Slide 39: AMBA AHB Arbiter Signal Description
Name | Source | Description
HBUSREQx Bus Request | Master | bus Master가bus에 대한 access를 요청할 때 사용된다. 각각의 bus master는 각각 HBUSREQx라는 interface를 가지게 되며, Arbiter는 최고 16개의 Master를 다룰 수 있다. 즉HBUSREQ[15:0]까자 사용할 수 있다.
HLOCKx | Master | bus Request신호와 동시에 인가된다. master가burst trans를 하려고 할 때, 중간에 다른 Master에게 bus의 소유를 넘기지 않을 것을 위해서 사용. Locked transfer의 첫번째 전송이 시작되면 Arbiter는 현재의 전송을 끝마 치기 전에는 다른 Master에게 bus의 사용권을 넘겨주지 않을 것이다.
HMASTER[3:0] | Arbiter | 현재 어떤 Maser가 선택 되어져 있는 가는 HMASTER[3:0]신호를 이용해 서 알 수 있다. 이것은 master들이 연결되는 MUX에 사용 되어진다. Maser number는 또한 SPLIT-capable slave에 의해서도 주어진다. 이것은 Master로 하여금 SPLIT 전송을 마무리 할 수 있도록 하는데 사용된다.
HMASTLOCK | Arbiter | HMASTLOCK 신호는 현재 전송하는 것이 locked transfer인지를 알려준다. 이것은 address와control signal과 동시에 나오게 된다.
HSPLIT[15:0] | Slave (SPLIT-capable) | 16bit의Split bus는SPLIT-capable slave에 의해서 주어진다. 이를 통해서 SPLIT 전송을 마무리 할 수 있도록 하는데 사용된다.
HGRANTx | Arbiter | Grant 신호는 arbiter에 의해서 발생된다. 이것은 가장 높은 priority를 가진 master에게만 HIGH를 준다. 그렇지만 Grant를 얻었다고 해서 바로 전송을 시작할 수 있는 것은 아니다. HREADY가HIGH일 때에만 비로소 전송을 시 작 할 수 있게 된다.

## Slide 40: Requesting Bus Access
Arbiter는 Request 신호를 매번 cycle의 rising edge에서 sampling하게 된다. 그 때마다 내부 priority algorithm을 가지고서 다음 grant를 결정하게 된다.
보통의 경우에 있어서 Arbiter는burst가 끝났을 때에 grant신호를 바꾸게 된다. 그렇지만 어떤 경우에 있어서는 burst를 갑자기 종료하고 다른 priority가 높은 master에게 access를 넘기기도 한다.
이와 같은 이유에서 원래는 burst를 위해서 한번만 Request를 하면 되지만, Re-Request를 해야 하는 경우가 발생하게 된다. 즉 중간에 burst가 종료되었으면, 그 나머지를 전송하기 위해서 Master는 다시 Request를 해야 한다. 예를 들어 처음에 8개의 전송을 하다가 4개까지 전송하고 중단 되었다면 4개짜리 burst나 1개짜리 burst를 4번 요청하는 등의 방법으로 새로운 burst를 시작해야 한다.
만약 아무런 Request가 없는 경우에도 Grant의 어떠한 bit는 항상 HIGH로 setting을 해주어야 하는데 이를 위해서 Default Master가 필요하다. 이 때는 Request를 하지 않는 경우 이므로 Master의 HTRANS 값은 IDLE상태를 나타내야 한다.

## Slide 41: Granting Bus Access with no wait states
HREADY가 HIGH일 때 HMASTER[3:0] 값이 바뀌면서 전송을 시작하게 될 것이다. 이에 대한 그림이 그림 3-4에 나와있다

## Slide 42: Data bus ownership

## Slide 43: Reset
HRESETn 신호는 AHB에 있어서 유일한 active LOW signal이다. Reset은 언제나 발생할 수 있지만 AHB가 알게 되는 것은 HCLK의 rising edge에서 sampling하게 된다. Reset이 되는 동안에 HTRANS[1:0]은 IDLE을 나타내어야 하며 address와 control signal들은 valid level에 있어야 한다.

## Slide 44: AHB bus interface

## Slide 45: AHB bus master interface

## Slide 46: AHB bus arbiter interface

## Slide 47: AHB bus decoder interface

## Slide 48: AMBA APB
  Minimal power consumption and reduced interface complexity
  Handles the bus handshake and control signal retiming
  Low bandwidth and do not require the high performance of a pipelined bus interface.
  All signal transitions are only related to the rising edge of the clock
Notes: APB bridge는 Advanced Peripheral Bus상의 유일한 버스 마스터이다. APB bridge는 ASB의 slave로서 decoder에서 APB가 선택이 되었을 때는 APB 상에서 마스터의 역할을 하게 된다
APB는 저전력 소모를 위해 최적화 및 인터페이스의 복잡도를 최소화.
APB bridge는 slave module로 local peripheral bus를 대신해서 bus handshake와 신호 retiming을 조정한다.
고성능이 필요하지 않는 장비를 위해 사용된다.
the APB is a low-power extension to the AHB/ASB
􀂊 APB appears as a local secondary bus encapsulated as
a single AHB/ASB slave device
􀂊 APB bridge acts as slave and handles necessary handshake
control and bus retiming
􀂊 APB bridge proves latching of all addresses, control and
data
􀂊 APB should be used to handle low-bandwidth devices
􀂊 APB slave devices have following characteristics:
􀂊 address and control valid throughout the access (nonpipelined)
􀂊 zero-power interface during non-peripheral bus activity
􀂊 timing can be provided by decode with strobe timing (unclocked
interface)
􀂊 write data valid for the whole access (allowing glitch-free
transparent latch implementation)

## Slide 49: AMBA APB
  All other modules on the APB are APB slaves.
  The APB slaves have the following interface specification
    address and control valid throughout the access (unpipelined)
    zero-power interface during non-peripheral bus activity (peripheral bus is static when not in use)
    timing can be provided by decode with strobe timing (unclocked interface)
    write data valid for the whole access (allowing glitch-free transparent latch implementations)
Notes: APB에 연결되는 모든 신호는 rising-edge에서 동작한다.
APB slave의 interface 특성
a. address와 control은 access를 통해 가능하다(unpipelined)
b. non-peripheral bus 동작은 전력 소모가 없는 interface.(peripheral bus는 사용되지 않을 때는 정적인 상태이다.)
c. timing 정보는 strobe timimg을 decede함으로써 제공될 수 있다.(unclocked interface)
d. 전 과정을 통해 write data는 가능하다.(allowing glitch-free transparent latch implementation)

## Slide 50: AMBA APB
IDEL : Peripheral bus의 default state
SETUP : 전송 요구와 있을 때 PSELx에 의해 bus는 SETUP 상태로 옮아가게 되며, 한 clock cycle만 유지하고 ENABLE 상태로 바뀐다.
ENABLE : PENABLE 신호가 보내지며, 더 이상의 전송 요구가 없으면 IDLE 상태로 바뀐다. SETUP에서 ENABLE로 상태가 바뀔 때, address, write 그리고 select 신호는 안정된 상태를 유지한다.

## Slide 51: Write transfer
Write transfer는 address, write data, write 신호와 select 신호가 PCLK의 rising과 함께 바뀌며 시작된다. 첫 cycle은 SETUP으로 두 번째 rising에 PENABLE 신호가 생성된다. 이 cycle 동안 전송은 완료되며, address, data, 그리고 control 신호는 그 값을 유지한다.
PENABLE 신호는 전송의 완료와 함께 LOW로 되며, 이 때 PSEL 또한 LOW가 된다.
전력 소모를 줄이기 위해 그 다음 access까지 address와 write 신호는 변하지 않는다

## Slide 52: Read transfer

## Slide 53: APB bridge
Bridge 만이 APB에서 master의 역할을 한다. 또한 bridge는 AHB에서의 slave.
a. address를 AHB로부터 APB로 전달
b. address를 decode하고 PSELx를 발생. transfer하는 동안 한 slave만 선택
c. write transfer동안 AHP에서 APB로 data를 이동.
d. read transfer동안 APB에서 AHB로 data를 이동.
e. 전송을 위한 timing 신호인 PENABLE 신호를 생성.

## Slide 54: APB bridge transfer

## Slide 55: AMBA
AMBA AHB Features
Bus name | AMBA AHB
Data bus width | 32-64-128-256 bit
Address bus width | 32 bit
architecture | Multi Master / Multi Slave
Data bus protocol | Single read/write transfer, Burst transfer (4,8,16 Bytes) Pipelined Byte/Half-word/word transfer support
Timing | Synchronous
Interconnection | Multiplexed implementation
Supported interconnections | Non-tristate, Separate data read & write bus required

## Slide 56: AMBA
AMBA APB Features
Bus name | AMBA APB
Data bus width | 8-16-32 bit
Address bus width | 32 bit
architecture | Single Master (bridge) / Multi Slave
Data bus protocol | 2 cycle read/write transfer, No Burst transfer Non-Pipelined
Timing | Synchronous
Interconnection | Not defined
Supported interconnections | Non-tristate bus recommended Separate data read & write bus recommended
Power | Zero power when not in use

## Slide 57: APB Interface Diagrams
recommended to implement APB data bus as
􀂊 multiplexed or
􀂊 OR-bus schema
􀂊 tri-state is possible but not recommended

## Slide 58: Read Transfer from AHB to APB
Notes: for a write transfer the data can be latched when:
􀂊 risinf edge of PCLK, when PSEL is high
􀂊 rising edge of PEANBLE, when PSEL is high

## Slide 59: AMBA Test Interface
Notes: AMBA test philosophy allows individual modules in
the system to be tested in isolation
􀂊 modules are designed to be tested by bus transfers only
􀂊 test harness provides access to inputs/outputs of
modules not already connected to bus

## Slide 60: AMBA Test Interface Write Cycle

## Slide 61: Coreconnect TM Bus Architecture
Coreconnect
  CoreConnect is an IBM-developed on-chip bus communications link that enables chip cores from multiple sources to be interconnected to create entire new chips.
  The CoreConnect technology eases the integration and reuse of processor, system, and peripheral cores within standard product platform designs to achieve overall greater system performance.

## Slide 62: Coreconnect TM Bus Architecture
Coreconnect
Notes: Figure 5 illustrates how the CoreConnect architecture can be used to interconnect macros in a PowerPC
440 based SOC. High performance, high bandwidth blocks such as the PowerPC 440 CPU core, PCI-X
Bridge and PC133/DDR133 SDRAM Controller reside on the PLB, while the OPB hosts lower data rate
peripherals. The daisy-chained DCR bus provides a relatively low-speed data path for passing
configuration and status information between the PowerPC 440 CPU core and other on-chip macros.

## Slide 63: Coreconnect TM Bus Architecture
Coreconnect
  The CoreConnect bus architecture includes :
    processor local bus (PLB)
    on-chip peripheral bus (OPB)
    device control register bus (DCR)
Notes:     processor local bus (PLB)
  The PLB bus addresses the high performance, low latency system modules and provides the design flexiblity needed in a highly integrated SOC.
    on-chip peripheral bus (OPB)
  The OPB bus is optimised to connect to lower speed peripherals and low power consumption.
    device control register bus (DCR)
  The Device Control Register (DCR) bus is designed to transfer data between the CPU's general purpose registers (GPRs) and the DCR slave logic's device control registers (DCRs). Lower performance status and configuration registers are typically read and written through the Device Control Register (DCR) Bus. The DCR provides a maximum throughput of one read or write transfer every two cycles and is a fully synchronous bus typically implemented as a distributed multiplexer.

## Slide 64: Coreconnect TM Bus Architecture
Coreconnect PLB Features
Bus name | Coreconnect PLB
Data bus width | 32-64-128-256 bit
Address bus width | 32 bit (With address pipelining, reducing latency)
architecture | Multi Master (Max 8) / Multi Slave
Data bus protocol | Single read/write transfer, Burst transfer (16, 64 Bytes) Overlapped read/write (2 transfers/cycle) Pipelined
Timing | Fully Synchronous
Interconnection | Crossbar switch
Supported interconnections | Non-tristate, Separate data read & write bus
Notes: Address bus width :
Address pipelining that reduces bus latency by overlapping a new write request with an ongoing
write transfer and up to three read requests with an ongoing read transfer.
Data bus protocol :
Concurrent read and write transfers yielding a maximum bus utilization of two data transfers per clock

## Slide 65: Coreconnect TM Bus Architecture
Coreconnect OPB Features
Bus name | Coreconnect OPB
Data bus width | 8-16-32 bit
Address bus width | 32 bit
architecture | Multi Master (arbiter) / Multi Slave
Data bus protocol | Dynamic bus sizing possible Single read/write transfer, Burst transfer Retry support DMA support
Timing | Fully Synchronous
Interconnection | Multiplexed implementation
Supported interconnections | Non-tristate, Separate data read & write bus
Notes: Dynamic bus sizing to support byte, half-word and word transfers

## Slide 66: Coreconnect TM Bus Architecture
Coreconnect DCR Features
Bus name | Coreconnect DCR
Data bus width | 32 bit
Address bus width | 10 bit
Interconnection | Multiplexed implementation
Purpose | Transfer data between the CPU’s general purpose registers (GPR) and other (peripheral) registers, not meant for real data transfers Designed to reduce load on PLB and OPB

## Slide 67: WISHBONE
Overview
  The WISHBONE System-on-Chip (SoC) interconnection architecture for portable IP cores is a flexible design methodology for use with semiconductor IP cores.
WISHBONE System-on-Chip Interconnect Architecture
  Simple architecture
  Truly open specification
    Silicore placed specifications in the public domain
    In September 2002 Silicore handed stewardship over to OpenCores
  Patent & Royalty free
Notes: 1. Its purpose is to foster design reuse by alleviating System-on-Chip integration problems. This is accomplished by creating a
common interface between IP cores. This improves the portability and reliability of the system, and results in faster time-to-market for the end user.
1. Its purpose is to foster design reuse by alleviating System-on-Chip integration problems. This is accomplished by creating a
common interface between IP cores. This improves the portability and reliability of the system, and results in faster time-to-market for the end user.

## Slide 68: WISHBONE
WISHBONE Interconnect Architecture
Notes: SYSCON : Generates clock and reset
INTERCON :IP core that connects one or more masters to one or more slaves
MASTER : Interface that is capable of generating bus cycles
SLAVE : Interface that is capable of responding to bus cycles

## Slide 69: WISHBONE
The point-to-point interconnection
The data flow interconnection
Notes: 1. The point-to-point interconnection is the simplest way to connect two WISHBONE IP cores together.
The point-to-point interconnection allows a single MASTER interface to connect to a single SLAVE interface.
2. The data flow interconnection is used when data is processed in a sequential manner. Each IP core in the data flow architecture has both a MASTER and a SLAVE interface. Data flows from core-to-core. Sometimes this process is called pipelining. The data flow architecture exploits parallelism, thereby speeding up execution time.

## Slide 70: WISHBONE
Shared Bus interconnection
Crossbar switch interconnection
Notes: 3. The shared bus interconnection is useful for connecting two or more MASTERs with one or
more SLAVEs. A block diagram is shown in Figure A-4. In this topology a MASTER initiates
a bus cycle to a target SLAVE. The target SLAVE then participates in one or more bus cycles
with the MASTER.
The main advantage to this technique is that shared interconnection systems are relatively compact.
Generally, it requires fewer logic gates and routing resources than other configurations,
especially the crossbar switch.
4. The crossbar switch interconnection is used when connecting two or more WISHBONE MASTERs
together so that each can access two or more SLAVEs. A block diagram is shown in Figure
A-5. In the crossbar interconnection, a MASTER initiates an addressable bus cycle to a target
SLAVE. An arbiter (not shown in the diagram) determines when each MASTER may gain
access to the indicated SLAVE. Unlike the shared bus interconnection, the crossbar switch allows
more than one MASTER to use the interconnection (as long as two MASTERs don’t access
the same SLAVE at the same time).

## Slide 71: WISHBONE
WISHBONE Features
Bus name | Wishbobe
Data bus width | 8 to 64 bits
Address bus width | 8 to 64 bits
architecture | Multi Master / Multi Slave
Data bus protocol | Single read/write transfer, Block transfer cycle RMW(Read-Modify-Write) cycle Up to one data transfer per clock cycle
Timing | Synchronous
Interconnection | Point-to-Point, Data flow, Shared bus, Crossbar switch
Supported interconnections | Unidirectional bus, Bi-directional bus Multiplexer based interconnections Tristate based interconnections
Notes: The BLOCK transfer cycles perform multiple data transfers.
The RMW (read-modify-write) cycle is used for indivisible semaphore operations. During the
first half of the cycle a single read data transfer is performed. During the second half of the cycle
a write data transfer is performed.
The BLOCK transfer cycles perform multiple data transfers.
The RMW (read-modify-write) cycle is used for indivisible semaphore operations. During the
first half of the cycle a single read data transfer is performed. During the second half of the cycle
a write data transfer is performed.

## Slide 72: Sonics µNetworks
µNetwork Features
  The key concept governing the Sonics architecture is the combining :
    a fully pipelined, fixed-latency bus
    a Time-Division Multiple Access (TDMA) bandwidth allocation scheme into a single communications protocol
The main protocols are :
  Open Core Protocol(OCP) Interface
  SiliconBackplane µNetwork
Notes: 1. The former (fully pipelined, fixed-latency bus) is common inside CPU designs, while the latter (TDMA bandwidth allocation scheme) is prevalent in communications
systems. Combining both concepts produces a protocol with high performance and reliable communications over a wide variety of systems and
subsystems. Both latency-sensitive CPU cores and real-time multimedia and networking cores benefit from this design approach.
Pipeline :
A write transfer, for example, requires sending both address and data to the receiving device. Because the write data and the read data both share the
same wires (separating them does not increase bandwidth, since there is only one set of address wires), the write data is sent during the same cycle as the
read data. The SB(SiliconBackplane) bus has separate wires for command-related fields (command and address) and data-related fields (data and response).
Fixed-laytency bus :
The SB is a fixed-latency bus. When a transfer cannot be completed in time, the transfer is retried later. This decouples the different data streams from
one another, since wait states are never inserted in the bus pipeline. Minimizing repeated transfers avoids wasting bandwidth. To accomplish this, the
latency of the SiliconBackplane µNetwork is a tuning parameter of the system, allowing the designer to choose a value based on the application
characteristics.
TDMA :
The TDMA approach provides fast access to variable-latency subsystems without the system modeling uncertainties associated with wait states.
This flexible TDMA-based approach provides enough bandwidth to unify system communications; thereby simplifying the system design while
increasing flexibility.

## Slide 73: Sonics µNetworks
The advantages of the Sonics µNetwork architecture
  Configured to the Application
  Cost and Performance
  Verification, Validation, and Testing
Notes: Configured to the Application :
Sonics µNetworks enable the design team to optimize the design for maximum
flexibility or minimum die size. Individual configuration features can be fixed
at compile time or be left as re-programmable to be selected at runtime.
Cost and Performance :
A µnetwork produces SOCs that are smaller, provide higher performance, and
have higher functionality than those designed using current approaches.
The structure provided by the SiliconBackplane µNetwork greatly simplifies
complicated physical design issues. All of the long inter-core wiring in the
SOC design has been moved into the SiliconBackplane µNetwork.
The agents are distributed across the chip so that OCP wires become short nets. Since
the long wires are inside the SiliconBackplane, all of the drivers, receivers,
and nets can be tuned simultaneously to meet the required performance,
without affecting any of the IP cores
Verification, Validation, and Testing :
Verification, validation, and testing are some of the greatest challenges in
SOC design. Because the Sonics µNetworks unifies all IP core communication
through the shared SiliconBackplane µNetwork, all data and control traffic
can be observed and controlled.
This allows the core to be tested in isolation, and guarantees
that the same test vectors can be used for a given IP core regardless of the
SOC design.

## Slide 74: Sonics µNetworks
The SiliconBackplane µNetwork (SB) consists of a physical interconnect bus configured with a combination of agents.
Notes: MicroNetwork is composed of:
Agents
Connected together via SiliconBackplane protocol
Connected to IP Cores via OCP socket protocol

## Slide 75: Sonics µNetworks
InitiatorAgent
  This agent serves as the interface between the SB and an attached master core such as a CPU, DSP core or DMA controller.
TargetAgent
  This agent interfaces the physical bus to a slave device such as memory and UART engines to the SiliconBackplane µNetwork
ServiceAgent
  The ServiceAgent is an enhanced InitiatorAgent that provides debug and test capabilities
Notes: Initiatoragent :
The InitiatorAgent accepts requests from the Open Core Protocol, then transmits SiliconBackplane requests and processes the responses. It receives
responses from the addressed target and returns responses to its subsystem core.
Targetagent :
This agent serves as the bridge between the SB and the OCP.
Serviceagent :
This agent is used for reset, test, and debug operations

## Slide 76: Sonics µNetworks
SiliconBackplane is composed of :
  System Bandwidth
    Latency
    Bandwidth allocation
  Thread management
  Arbitration
  addressing
Notes: System bandwidth :
The total system bandwidth, the allocation of that bandwidth, and the SiliconBackplane latency can all be
varied to build in system flexibility.
- Latency : the SB is fully pipelined, multiple transfers may be overlapped. the latency of the SiliconBackplane µNetwork will
typically be 2-4 SB cycles, but only one or two CPU cycles.
- Bandwidth allocation : Once the bandwidth and latency numbers have been selected, the bandwidth
must be allocated to the different cores. The allocation is on a cycle by cycle
basis that is based on a TDMA time wheel with a fixed number of time slots.
Thread :
The SiliconBackplane µNetwork uses the concept of a connection ID to identify
an initiating thread within the system. Each thread at every initiator
core's OCP is assigned a system-wide unique connection ID, regardless of
whether the initiator OCP interface is single or multi-threaded.
Arbitration :
Only InitiatorAgents arbitrate for access to the µnetwork. TargetAgents need
not arbitrate for the right to return data or response, since the IM (Initiatoragent Module) that issued
the command to the TM (Targetagent Module) allocated time on the data/response fields. µNetwork
access is defined by a two-level arbitration scheme. The first level of arbitration
is based on a Time-Division Multiple Access (TDMA) mechanism. A
second, lower priority access scheme is based on a round-robin token passing
mechanism.
Address :
All transactions over the SB are memory–mapped and all non-idle commands
require addresses. Unique address spaces must be assigned to all agents.
When a target matches the address on the SB, a determination is made on
whether the address is intended for the subsystem core or for internal configuration
registers in the TargetAgent.

## Slide 77: Open Core Protocol
An overview of Open Core Protocol
  The Open Core Protocol defines a high-performance, bus-independent interface between IP cores.
Open Core Protocol
  Achieve the goal of IP design reuse.
  Optimizes die area
  Simplifies system verification and testing
Notes: The Open Core Protocol defines a high-performance, bus-independent interface between IP cores that reduces design time, design risk, and manufacturing costs for SoC designs.
1. Achieve the goal of IP design reuse. The OCP transforms IP cores making then independent of the architecture and design of the systems in which they are used.
2. Optimizes die area by configuring into the OCP only those features needed by the communicating cores.
3. Simplifies system verification and testing by providing a firm boundary around each IP core that can be observed, controlled, and validated.
OCP provides a combined communication protocol and hardware connection scheme for SOC logic blocks. As a protocol, OCP provides a minimal command set for memory-mapped, split-transaction activities such as read, write, and read exclusive. These atomic activities occur over threads communication channels that guarantee the response sequence order matches that of the original associated requests. Thread tags accompanying memory-mapped requests therefore providing an efficient way to present requests from an OCP master interface to an OCP slave interface.
The OCP interface addresses communications between the functional units (or IP cores) that comprise a SoC. The OCP provides independence from bus protocols without having to sacrifice high-performance access to on-chip interconnects. By designing to the interface boundary defined by the OCP, you can develop reusable IP cores without regard for the ultimate target system.

## Slide 78: Open Core Protocol
Open Core Protocol
Notes: The OCP defines a point-to-point between two communicating entities, such as IP cores and bus interface modules (bus wrappers). For two entities to communicate in a peer-to-peer fashion, there need to be two instances of the OCP connecting them.
The characteristics of the IP core determine whether the core needs master, slave, of both sides of the OCP (the wrapper interface modules must act as the complementary side of the OCP for each connected entity).
A transfer across system occurs as follows
A system initiator presents command, control and possibly data to its connected slave.
The interface module plays the request across the on-chip bus system.
The OCP does not specify the embedded bus functionality.
The receiving converts the OCP request into an embedded bus transfer.
The receiving bus wrapper interface module converts the embedded bus operation into a legal OCP command.
The system target receives the command and takes the requested action.

## Slide 79: Open Core Protocol
Operation of OCP 1
  Point-to-Point synchronous interface
  Bus independence
  Commands
  Address/Data
  Pipelining
Notes: Point-to-Point synchronous interface : To simplify timing analysis, physical design, and general comprehension, the OCP is composed of uni-directional signals driven with respect to, and sampled by the rising edge of the OCP clock. The OCP is fully synchronous and contains no multi-cycle timing paths. All signals other than the clock are strictly point-to-point.
Bus independence : A core utilizing the OCP can be interfaced to any bus. A test of any bus-independent interface is to connect a master to a slave without an intervening on-chip bus.
Commands : There are two basic commands. Read and Write and five command extensions. The WriteNonPost and Broadcast commands have semantics that are similar to the write command. A WriteNonPost explicitly instructs the slave not to post a write. Broadcast is typically useful only for slaves that are in turn a master on another communication medium. The other command extensions, ReadExclusive, ReadLinked and WriteConditional, are used for synchronization between system initiators.
Address/Data : Wide widths, characteristic of shared on-chip address and data buses, make turning the OCP address and data widths essential for area-efficient implementation.
Pipelining : The OCP allows pipelining of transfers. To support this feature, the return of read data and the provision of write data may be delayed after the presentation of the associated request.

## Slide 80: Open Core Protocol
Operation of OCP 2
  Response
  Burst
  In-band information
  Threads and Connections
  Interrupts, Errors, and other Sideband signaling
Notes: Response : the OCP separates requests from responses. A slave can accept a command request from a master on one cycle and respond in a later cycle. The division of request from response permits pipelining.
Burst : To provide high transfer efficiency, burst support is essential for many IP cores. The extended OCP supports annotation of transfers with burst information.
In-band information : Cores can pass core-specific information in-band in company with the other information being exchanged. In-band extensions exist for requests and responses, as well as read and write data.
Threads and Connections : To support concurrency and out-of-order processing of transfers, the extended OCP supports the notion of multiple threads. Transactions within different threads have no ordering requirements, and so can be processed out of order.
Interrupts, Errors, and other sideband signaling : Different types of control signaling are required to coordinate data transfers or signal system events. Dedicated point to point data communication is sometimes required. Many devices also require the ability to notify the system of errors that may be unrelated to address/data transfers.

## Slide 81: Open Core Protocol
OCP interface signals
  Dataflow signal
  Sideband signal
  Test signal
The basic OCP signals
  A small set of the signals from the dataflow
The Optional OCP signals
  To support additional core communication requirements
Notes: A small set of the signals from the dataflow group called the basic OCP, is required in all OCP configurations. Optional signals can be configured to support additional core communication requirements. The optional dataflow signals are divided into simple and complex extensions. All sideband and test signals are optional.

## Slide 82: PI-Bus
An overview of Peripheral Interconnect Bus
  A European on-chip interconnection bus for silicon systems resulting from the ESPRIT Open Microprocessor Systems Initiative.
Target of PI-Bus
  High speed on-chip interconnect
  Promotion of design reuse
  Integration of designs from different organizations
Notes: The Peripheral Interconnect Bus (PI-Bus) is a European on-chip interconnection bus for silicon systems resulting from the ESPRIT Open Microprocessor Systems Initiative (OMI). Five major European semiconductor companies have licensed the PI-Bus: Advanced RISC Machines (ARM), Philips Semiconductors, SGS-Thompson Microelectronics, Siemens and Temic/Matra MHS.
The need for high-speed on-chip interconnect arises for a number of reasons, including, rapid progress towards systems on a chip, the growth of modular design methodologies, an increased silicon capacity, promotion of design reuse by bus based encapsulation and the integration of designs from different organizations.

## Slide 83: PI-Bus
High performance Features
  Synchronous
  Non-multiplexed address and data scheme
  Pipelined burst mode operation
  Only technology limitations clock speeds
  Multi-master capability
Notes: The PI-Bus is suitable for very large scale ICs using deep submicron technologies and modular architectures. Its high bandwidth and low overhead means that it is ideal to handle high-speed on-chip intercommunication, such as connecting processor cores, memories, co-processors and I/O controllers. The peak transfer rate is 200 MBytes/sec with a 50-MHz clock. The address and data buses are scaleable up to 32-bits. Licensing for the PI-Bus is available at a nominal cost. The PI-Bus is an open protocol oriented towards fast agent access and high-transfer bandwidth. The low-overhead protocol guarantees short response times for bus access which are needed for time-critical applications.

## Slide 84: PI-Bus
PI-Bus
Notes: A model is provided for the master, slave and bus control unit. The BCU model is a complex example that can be simplified for a small PI-Bus system. To provide compatibility with widely different platforms we have used structural VHDL to link PI-Bus modules.

## Slide 85: PI-Bus
PI-Bus VHDL toolkit methodlogy
  Slave, master and master/slave
  Bus control unit
  Master based test support
  Transaction spy
Notes: PI-Bus VHDL toolkit methodlogy
1. Encapsulates the existing bus models and introduces new test based models that are used at every stage of the bus based component design
2. Test frameworks/systems are included to facilitate rapid prototyping of proposed designs
3. Toolkit methodology offers RTL level VHDL that has been implemented repeatedly and successfully in silicon combined with a set of guidelines
Slave, Master and Master/Slave : Agents of a bus system
Bus Control Unit : Essential component of many bus based system
Master based test support : Circuits to exercise the bus and emulate real bus traffic
Transaction Spy : Automatic monitoring of bus activity
Each transaction is monitored to identify errors both within the protocol and outside.
Changes to the interface models can be continuously verified as to have not broken the interface operation.
A report is produced to a file that indicates problems independently to the transcript window of the simulator, this prevents the problems from being missed in a mass of messages found in many real simulation environments.
Removes the need for a designer to read through all the cycles of every PI-Bus transaction to ensure correct operation.
PCI Bus SPY implemented by University of Sussex and later the PI-Bus version implemented by Matra MHS organization within OMI/SMILE.

## Slide 86: CoreFrame (Palmchip)
The CoreFrame architecture is a low-power, high-performance on-chip interconnect architecture for integration of SOC (system-on-chip) blocks in a synthesis friendly environment.
Notes: CoreFrame
from Palmchip Company is a nonpipelined bus which also has two independent bus types: Mbus for memory transfer
and Palmbus for I/O devices

## Slide 87: CoreFrame (Palmchip)
CoreFrame Features
  PalmBus : Designed for lowspeed accesses from the CPU core to peripheral blocks.
  MBus : Designed for highspeed accesses to shared memory from the CPU core and peripheral blocks.
  The CoreFrame architecture is processor independent.
  The PalmBus Controller and Cache both act as a bridge between the CPU subsystem and the CoreFrame subsystem.
Notes: Palmbus & Mbus :
The PalmBus and MBus are independent parallel “busses”, rather than a hierarchy of
busses. Concurrent activity may be achieved on both busses, maximizing available
bandwidth resources.
processor independent :
The CPU and its dedicated memory are shown as part of an independent CPU subsystem.
This reduces bandwidth constraints on the shared memory. Use of a cache further minimizes CPU accesses to the
shared memory.

## Slide 88: CoreFrame (Palmchip)
CoreFrame channels interface between the MBus and the Memory subsystem and provide a number of functions :
Notes: The channel view of the CoreFrame architecture emphasizes the point-to-point nature of its
interconnects,
Each DMA peripheral has a connection to a dedicated channel. The channel handles all
interfacing between the peripheral and the MBus.
the channel interface looks basically like a FIFO.
Using the channels, it is straightforward to integrate peripherals that require DMA because
the peripheral does not need to worry about many system issues, including pipelining,
memory addressing, arbitration and endianness.
Address control is performed by simply passing the address from the channel interface to
the MBus.
Request/grant control generally works with the channel ready logic for flow control between
the peripheral and the FIFO.

## Slide 89: 참고문헌
[1] 이진, 박신종, “ Principle of SoC (II)”, SITI Newsletters, 제1권 2호, 2002
[2] AMBA Specification Revision 2.0, ARM Ltd., 1999
[3] IBM, http://www.ibm.com/chips/products/coreconnect/
[4] Opencore, “WISHBONE, Revision B.3 Specification”, http://www.opencores.org/wishbone/
[5] OCP-IP association, “OCP IP Open Core Protocol Specification 2.0”, 2003
[6] Sonics, “Sonics µnetworks Technical Overview”, June, 2000
[7] PalmChip Corp., “CoreFrame view white paper: Overview of the CoreFrame Architecture”. Http://www.palmchip.com
[8] http://www.sussex.ac.uk/Units/vlsi/projects/pibus/
[9] OMI. “PI Bus v3.1 Documentation”, 1996

## Slide 90
M. Shalan and V. Mooney, "Hardware Support for Real-Time Embedded Multiprocessor System-on-a-Chip Memory Management," CODES'02, pp 79-84, May 2002
Baghdadi, A.; Lyonnard, D., Zergainoh, N.-E., Jerraya, A.A. “An efficient architecture model for systematic design of application-specific multiprocessor SoC” DATE, 2001. pp 55 -62 , March 2001
Gharsalli, F., Lyonnard, D., Meftali, A., Rousseau, F., Jerraya, A.A, “Unifying memory and processor wrapper architecture in multiprocessor SoC design”, ISSS 2002, Page(s): 26 -31, Oct, 2002
Christou, C.S. “Fast computations on a low-cost DSP-based shared-memory multiprocessor system” Electronics, Circuits and Systems, 17-20, Page(s): 189 -192. Dec. 2000
www.arm.com
www.parthusceva.com
http://tima-cmp.imag.fr/Homepages/jerraya/jerraya.html
http://www.aijisystem.com/index_korea.htm, “scorpio user’s manual”