## Slide 1: Module 13 Interconnect-Centric SoC Platform Architecture
조준동 교수
(성균관대학교)

## Slide 2: 목차
Introduction to network
On-chip interconnection network
  Network topologies
Switching
Routing
Buffer scheme
Congestion Control
Protocol
  layer
On-Chip network examples

## Slide 3: Networks
Goal: Communication between computers
Eventual Goal: treat collection of computers as if one big computer, distributed resource sharing
Theme: Different computers must agree on many things
  Overriding importance of standards and protocols
  Fault tolerance critical as well
Warning: Terminology-rich environment

## Slide 4: Interconnections (Networks)
Examples :
  Wide Area Network (ATM): 100-1000s nodes; ~ 5,000 kilometers
  Local Area Networks (Ethernet): 10-1000 nodes; ~ 1-2 kilometers
  System/Storage Area Networks (FC-AL): 10-100s nodes; ~ 0.025 to 0.1 kilometers per link
a.k.a.
network,
communication subnet
a.k.a.
end systems,
hosts
Interconnection Network

## Slide 5: HW Interface Issues
Where to connect network to computer?
  Cache consistent to avoid flushes? (=> memory bus)
  Latency and bandwidth? (=> memory bus)
  Standard interface card? (=> I/O bus)
  MPP => memory bus; LAN, WAN => I/O bus
$
CPU
L2 $
Memory Bus
Memory
Bus Adaptor
I/O bus
I/O
Controller
I/O
Controller
Network
ideal: high bandwidth,
low latency,
standard interface
Network

## Slide 6: SW Interface Issues
How to connect network to software?
  Programmed I/O?(low latency)
  DMA? (best for large messages)
  Receiver interrupted or received polls?
Things to avoid
  Invoking operating system in common case
  Operating at uncached memory speed (e.g., check status of network interface)

## Slide 7: Connecting Multiple Computers
Shared Media vs. Switched: pairs communicate at same time: “point-to-point” connections
Aggregate BW in switched network is many times shared
  point-to-point faster since no arbitration, simpler interface
Arbitration in Shared network?
  Central arbiter for LAN?
  Listen to check if being used (“Carrier Sensing”)
  Listen to check if collision (“Collision Detection”)
  Random resend to avoid repeated collisions; not fair arbitration;
  OK if low utilization
(A. K. A. data switching
interchanges, multistage
interconnection networks,
interface message processors)

## Slide 8: Networks Background
Facets people talk a lot about:
  direct (point-to-point) vs. indirect (multi-hop)
  topology (e.g., bus, ring, DAG)
    How switches and nodes are connected
  routing algorithms
    Determines the route from source to destination
  switching (aka multiplexing)
    How a message traverse the route
  Flow control
    Schedules the traversal of the message over time
What really matters:
  latency
  bandwidth
  cost
  reliability

## Slide 9: More Network Background
Connection of 2 or more networks: Internetworking
3 cultures for 3 classes of networks
  WAN: telecommunications, Internet
  LAN: PC, workstations, servers cost
  SAN: Clusters, RAID boxes: latency (System A.N.) or bandwidth (Storage A.N.)
Try for single terminology
Motivate the interconnection complexity incrementally

## Slide 10: Network Performance Measures
Overhead: latency of interface vs. Latency: network

## Slide 11: Latency
Time(n) = Admission + Channel Occupancy + Routing Delay + Contention Delay
Admission
  is the time it takes to emit the message into the network.
Channel Occupancy
  is the time a channel is occupied.
Routing Delay
  is the delay for the route.
Contention Delay
  is the delay of a message due to contention.

## Slide 12: Local and Global Bandwidth
﻿b ... raw bandwidth of a link;
n ... message size;
nE ... size of message envelope;
w ... link bandwidth per cycle;
﻿Δ ... switching time for each switch in cycles;
wΔ ... bandwidth lost during switching;
C ... total number of channels;
For a kⅹk mesh with bidirectional channels:
Total bandwidth = (4k2 − 4k)b
Bisection bandwidth = 2kb

## Slide 13: Overhead, BW, Size
Msg Size
Delivered BW
How big are real messages?

## Slide 14: Basic Definitions
Message
  is the basic communication entity.
Flit
  is the basic flow control unit. A message consists of 1 or many flits.
Phit
  is the basic unit of the physical layer.
Direct network
  is a network where each switch connects to a node.
Indirect network
  is a network with switches not connected to any node.
Hop
  is the basic communication action from node to switch or from switch to switch.
Diameter
  is the length of the maximum shortest path between any two nodes measured in hops.
Routing distance between two nodes
  is the number of hops on a route.
Average distance
  is the average of the routing distance over all pairs of nodes.

## Slide 15: Network design issues
Topologies
Buffering
  Input buffers
  Output buffers
  Shared buffers
Routing
  Source routing
  Deterministic routing
  Adaptive routing
Deadlock
Control flow
Protocol

## Slide 16: Network Topology
Structure of the interconnect
Determines
  Degree: number of links from a node
  Diameter: max number of links crossed between nodes
  Average distance: number of hops to random destination
  Bisection: minimum number of links that separate the network into two halves (worst case)
Warning: these three-dimensional drawings must be mapped onto chips and boards which are essentially two-dimensional media
  Elegant when sketched on the blackboard may look awkward when constructed from chips, cables, boards, and boxes (largely 2D)
Networks should not be interesting!

## Slide 17: Centralized switch: Fully Connected Networks
Crossbar and Omega network
Omega network switch box

## Slide 18: Distributed switch
Linear Array, Rings, Multidimensional Meshes and Tori

## Slide 19: Distributed switch-cont’d
K-ary Tree and k-ary n-dimensional Fat Trees

## Slide 20: Distributed switch-cont’d
Butterflies
  Multistage: nodes at ends, switches in middle

## Slide 21: Butterflies
All paths equal length
Unique path from any input to any output
Conflicts that try to avoid
Don’t want algorithm to have to know paths
Cost of the network
  O(N logN)
  2-d layout is more difficult than for binary trees
  Number of long wires grows faster than for trees.
For each source-destination pair there is only one route.
Each route blocks many other routes.

## Slide 22: Characteristics of topologies
 | Number of Nodes | Switch degree | diameter | distance | Network cost | Total bandwidth | Bisection bandwidth
Bus | N | N | 1 | 1 | O(N) | b | b
crossbar | N | N | 1 | 1 | O(N2) | Nb | Nb
Linear Array | N | 2 | N-1 | ~2/3N | O(N) | 2(N-1)b | 2b
Torus | N | 2 | N/2 | ~1/3N | O(N) | 2Nb | 4b
K-ary d-cube | Kd | d | d(k-1) | ~d½(k-1) | O(N) | dNb | 2k(d-1)b
K-ary Tree | Kd (# of switch: ~ Kd) | K+1 | 2d | ~d+2 | O(N) | 2·2(N-1)b | kb
bufferfly | 2d (# of switch: ~ 2d-1d) | 2 | d+1 | d+1 | O(Nd) | 2ddb | (N/2)b
k-ary n-D Fat Tree | Kd (# of switch: ~ Kd-1d) | 2k | 2d | ~d | O(Nd) | 4kddb | 2kd-1b

## Slide 23: Projection of multi-d and k-ary
Efficient and regular 2-layout;
2-ary Tree Longest wires in resource width:

## Slide 24: Topologies of Super Computers

## Slide 25: Switching Techniques
Circuit Switching
  A real or virtual circuit establishes a direct connection between source and destination.
Packet Switching
  Each packet of a message is routed independently. The destination address has to be provided with each packet.
Store and Forward Packet Switching
  The entire packet is stored and then forwarded at each switch.
Cut Through Packet Switching
  The flits of a packet are pipelined through the network. The packet is not completely buffered in each switch.
Virtual Cut Through Packet Switching
  The entire packet is stored in a switch only when the header flit is blocked due to congestion.
Wormhole Switching
  is cut through switching and all flits are blocked on the spot when the header flit is blocked.

## Slide 26: Connection-Based vs. Connectionless
Telephone: operator sets up connection between the caller and the receiver
  Once the connection is established, conversation can continue for hours
Share transmission lines over long distances by using switches to multiplex several conversations on the same lines
  “Time division multiplexing” divide B/W transmission line into a fixed number of slots, with each slot assigned to a conversation
Problem: lines busy based on number of conversations, not amount of information sent
Advantage: reserved bandwidth

## Slide 27: Connection-Based vs. Connectionless
Connectionless: every package of information must have an address => packets
  Each package is routed to its destination by looking at its address
  Analogy, the postal system (sending a letter)
  also called “Statistical multiplexing”
  Note: “Split phase buses” are sending packets

## Slide 28: Switch Design

## Slide 29: Switch Scaling
Switches are wire dominated
Scaling with equal switch size by a factor s:
  number of transistors: s2
  number of I/O's: s
  speed of transistor: 1/s
  speed of wires: 1
  delay of the switch: 1
Scaling with equal I/O number by factor s:
  size of the switch: 1/s2
  speed of transistor: 1/s
  speed of wires: 1/s
  delay of the switch: 1/s

## Slide 30: Stacked Dimension Switch
Simple 2ⅹ2 building block can be repeatedly used;
in k-ary n-cubes we need n 2ⅹ2 switches
instead of nⅹn switches;
Changing dimension incurs additional delay;
Switching is very fast in the same dimension;

## Slide 31: Routing
Shared Media
  Broadcast to everyone, but switched Media needs real routing.
Virtual Circuit: circuit established from source to destination, message picks the circuit to follow
Arithmetic routing
  The destination address of the incoming packet is compared with the address of the switch and the packet is routed accordingly. (relative or absolute addresses)
Source based routing
  The source determines the route and builds a header with one directive for each switch. The switches strip off the top directive.
Table-driven routing
  Switches have routing tables, which can be configured.
Destination-based routing: message specifies destination, switch must pick the path
  Deterministic routing
    The route is determined solely by source and destination locations.
  Adaptive routing
    The route can be adapted by the switches to balance the load.
  Randomized routing
    pick between several good paths to balance network load
Minimal routing
  allows only shortest paths while non-minimal routing allows even longer paths.

## Slide 32: Deterministic Routing Examples
mesh: dimension-order routing
  (x1, y1) -> (x2, y2)
  first x = x2 - x1,
  then y = y2 - y1,
Multi-D cube: edge-cube routing
  X = xox1x2 . . .xn -> Y = yoy1y2 . . .yn
  R = X xor Y
  Traverse dimensions of differing address in order
tree: common ancestor
Deadlock free?
001
000
101
100
010
110
111
011

## Slide 33: Deadlock
Deadlock
  Two or several packets mutually block each other and wait for resources, which can never be free.
Livelock
  A packet keeps moving through the network but never reaches its destination.
Starvation
  A packet never gets a resource because it always looses the competition for that resource (fairness).

## Slide 34: Deadlock Situations
Head-on deadlock;
Nodes stop receiving packets;
Contention for switch buffers can occur with store-and-forward, virtual-cut-through and wormhole routing. Wormhole routing is particularly sensible.
Cannot occur in butterflies;
Cannot occur in trees or fat trees if upward and downward channels are independent;
Dimension order routing is deadlock free on k-ary n-arrays but not on tori with any n ≥ 1.

## Slide 35: Deadlock-free Routing
Two main approaches:
  Restrict the legal routes;
  Restrict how resources are allocated;
Number the channel cleverly
Construct the channel dependence graph
Prove that all legal routes follow a strictly increasing path in the channel dependence graph.

## Slide 36: Turn-Model Routing
What are the minimal routing restrictions to make routing deadlock free?
Three minimal routing restriction schemes:
  North-last
  West-first
  Negative-first
Allow complex, non-minimal adaptive routes.
Unidirectional k-ary n-cubes still need virtual channels.

## Slide 37: Adaptive Routing
The switch makes routing decisions based on the load.
Fully adaptive routing allows all shortest paths.
Partial adaptive routing allows only a subset of the shortest path.
Non-minimal adaptive routing allows also non-minimal paths.
Hot-potato routing is non-minimal adaptive routing without packet buffering.

## Slide 38: Store and Forward vs. Cut-Through
Store-and-forward policy: each switch waits for the full packet to arrive in switch before sending to the next switch (good for WAN)
Cut-through routing or worm hole routing: switch examines the header, decides where to send the message, and then starts forwarding it immediately
  In worm hole routing, when head of message is blocked, message stays strung out over the network, potentially blocking other messages (needs only buffer the piece of the packet that is sent between switches). CM-5 uses it, with each switch buffer being 4 bits per port.
  Cut through routing lets the tail continue when head is blocked, accordioning the whole message into a single switch. (Requires a buffer large enough to hold the largest packet).
Advantage
  Latency reduces from function of: number of intermediate switches X by the size of the packet to time for 1st part of the packet to negotiate the switches + the packet size ?interconnect BW

## Slide 39: Buffering-Input Buffering
Head-of line blocking limits output channel utilization to 60%.

## Slide 40: Buffering-Output Buffering

## Slide 41: Buffering-Shared Buffer Pool
Potential better utilization of buffers;
Speed of memory becomes limiting factor;

## Slide 42: Buffering-Virtual Channel Buffering
Dynamic virtual channel allocation can
  increase buffer utilization,
  reduce head-of-line blocking.
E.g. 256 nodes 2-ary butterfly with wormhole routing; 16 flits per link:
  no virtual channel: output channel saturation at 25% under random traffic;
  16 virtual channels: saturation at 80% traffic load;

## Slide 43: Congestion Control
Packet switched networks do not reserve bandwidth; this leads to contention (connection based limits input)
Solution: prevent packets from entering until contention is reduced (e.g., freeway on-ramp metering lights)
Options:
  Packet discarding: If packet arrives at switch and no room in buffer, packet is discarded (e.g., UDP)
  Flow control: between pairs of receivers and senders; use feedback to tell sender when allowed to send next packet
    Back-pressure: separate wires to tell to stop
    Window: give original sender right to send N packets before getting permission to send more; overlapslatency of interconnection with overhead to send & receive packet (e.g., TCP), adjustable window
  Choke packets: aka rate-based? Each packet received by busy switch in warning state sent back to the source via choke packet. Source reduces traffic to that destination by a fixed % (e.g., ATM)

## Slide 44: Protocols: HW/SW Interface
Protocol : Sequence of steps for SW
Internetworking: allows computers on independent and incompatible networks to communicate reliably and efficiently;
  Enabling technologies: SW standards that allow reliable communications without reliable networks
  Hierarchy of SW layers, giving each layer responsibility for portion of overall communications task, called protocol families or protocol suites
Transmission Control Protocol/Internet Protocol (TCP/IP)
  This protocol family is the basis of the Internet
  IP makes best effort to deliver; TCP guarantees delivery
  TCP/IP used even when communicating locally: NFS uses IP even though communicating across homogeneous LAN

## Slide 45: Software to Send and Receive
SW Send steps
  1: Application copies data to OS buffer
  2: OS calculates checksum, starts timer
  3: OS sends data to network interface HW and says start
SW Receive steps
  3: OS copies data from network interface HW to OS buffer
  2: OS calculates checksum, if matches send ACK; if not, deletes message (sender resends when timer expires)
  1: If OK, OS copies data to user address space and signals application to continue

## Slide 46: Protocol Family Concept
Key to protocol families is that communication occurs logically at the same level of the protocol, called peer-to-peer, but is implemented via services at the lower level
Danger is each level increases latency if implemented as hierarchy (e.g., multiple check sums)
Message
T
H
Message
T
H
Message
T
H
Message
Message
T
H
Message
T
H
T
H
Actual
Actual
Actual
Actual
Physical
Logical
Logical

## Slide 47: Protocol Family Concept
Key to protocol families is that communication occurs logically at the same level of the protocol, called peer-to-peer,
but is implemented via services at the next lower level
Encapsulation: carry higher level information within lower level “envelope”
Fragmentation: break packet into multiple smaller packets and reassemble
Danger is each level increases latency if implemented as hierarchy (e.g., multiple check sums)

## Slide 48: Connection of Networks
Bridges: connect LANs together, passing traffic from one side to another depending on the addresses in the packet.
  operate at the Ethernet protocol level
  usually simpler and cheaper than routers
Routers or Gateways: these devices connect LANs to WANs or WANs to WANs and resolve incompatible addressing.
  Generally slower than bridges, they operate at the internetworking protocol (IP) level
  Routers divide the interconnect into separate smaller subnets, which simplifies manageability and improves security
Cisco is major supplier; basically special purpose computers

## Slide 49: Protocol layer
Physical Layer
  Parameters:
    Physical distance
    Number of lines
    Activity control
    Buffers and pipelining
Data Link Layer
  Parameters:
    Line frequency versus switch frequency
    Buffering
    Error correction
    Power optimization encoding

## Slide 50: Protocol layer-cont’d
Network Layer
  Parameters:
    Link layer cell size vs. network layer packet size
    Network address scheme
    Routing algorithm
    Priority classes
    Error correction
  Network Layer Services
  Packet switched best effort service
    Packets are guaranteed to arrive
    Packet payload may be protected (4 levels of protection)
    Load dependable delay in the network
    Load dependable delay at the network access point
  Virtual circuit service
    Guaranteed bandwidth
    Guaranteed maximum delay
    Multicast circuits
    Based on packet switching service

## Slide 51: Protocol layer-cont’d
Session Layer
  Parameters:
    Task level communication primitives
    Message passing
    Shared memory based communication
    Synchronization
    Error correction
Application Layers
  Application specific communication services;
  E.g. the NoC operating system could use:
  Task/resource database access protocol
  Task migration protocol

## Slide 52: On-Chip network examples
Nostrum (KTH, Sweden)
  Toplogy:2-d mesh
  Wide (128 bits), short links
  Non-minimal adaptive hot-potato routing
  No buffering
  Service: Best effort, guaranteed latency virtual circuits
  Four data protection levels at link layer

## Slide 53: On-Chip network examples
Æthereal (Philips)
  Topology: probably low dimensional tree or mesh, or dedicated
  Deterministic source based routing
  Wormhole or virtual cut-through switching
  Input buffering
  Selectable connection features:
    Integrity
    Completion
    Ordering
    Bounds on latency, throughput and jitter

## Slide 54: On-Chip network examples
SPIN (UPMC/LIP6) in Paris
  Topology: fat tree
  Wormhole: switching
  Adaptive routing
  Input buffering
  Bidirectional 32 bit links
  Separate control network for configuration

## Slide 55: On-Chip network examples
Octagon at ST and UC San Diego
  Basic 8-node architecture
  Diameter: 2 hops
  Packet and circuit switching modes
  Source based routing with a 3 bit address in the header

## Slide 56: On-Chip network examples
XPipes at Bologna Univ.
  Source based routing
  Wormhole switching
  Long, pipelined links
  Output buffering
  Virtual channels
  Acknowledgment based flow control with retransmission

## Slide 57: On-Chip network examples
Proteo at Tampere university of technology
  Objective is to develop a flexible library of communication IPs that support various topologies and routing strategies
  Topology: Ring connecting local bus or star based clusters
  Virtual cut-through switching
  Routing: Table based
  Buffer: input and output buffering