## Slide 1: Bus Structures in Network-on-Chips
Interconnect-Centric Design for Advanced SoC and NoC - Chapter 8
Erno Salminen
11.10.2004

## Slide 2: Presentation Outline
Design choices
Problems and solutions
SoC examples
Conclusion
(References)

## Slide 3: Bus
(Shared) Bus
  Set of signals connected to all devices
  Shared resource - one connection between devices reserves the whole interconnection
  Most available SoC communication networks are buses
  Low implementation costs, simple
  Bandwidth shared among devices
  Long signal lines problematic in DSM technologies
A
A
A
A
A
A
a) single bus

## Slide 4: Hierarchical Bus
Hierarchical bus
  Several bus segments connected with bridges
  Fast access as long as the target is in the same segment
    Requires locality of accesses
  Theoretical max. speed-up = num of segments
  Segments either circuit or packet-switched together
    Packet-switching provides more parallelism with added buffering
B
A
A
A
A
A
A
b) hierarchical bus

## Slide 5: Signal Resolution
Figure 1. Signal resolution
b) mux-based
a) three-state
M = Master
S = Slave
c) AND-OR / OR
AND
M1
M2
S1
S2
AND
AND
AND
Control
Control
M1
BUF
M2
S1
S2
BUF
BUF
BUF
Global bus
MUX
MUX
Control
M1
M2
S1
S2
OR
Agent
Processor
local bus
Processor
Memory
Wrapper

## Slide 6: Structure
1. Hierarchical structures
2. Unidirectional (‘U’) or bidirectional (‘B’) links
3. Shared (‘S’) or point-to-point signals (‘P’)
Exceptions:
* In CoreConnect, data lines are shared, control lines form a ring
** In SiliconBackplane, data lines are shared, control flags are point-to-point
4. Synchronous (‘S’) or asynchronous (‘A’) transfers
5. Support for multiple clock domains
6. Test structures

## Slide 7: Transfers (1)
Pipelined transfer = Address is transferred before data
  More time for address decoding
  Address can be interleaved with last data of the previous transfer
Split transfer = Read operation is split into two write operations
  Agent A sends a read-request to agent B
  Bus is released, when agent B prepares the data
  When agent B is ready, it writes the data to agent A
t
rq addr
ret addr
addr
data
w addr
w data
ret data
w data
w addr
rq addr
ret addr
rq data
rq data
ret addr
...
pipeline
split transaction

## Slide 8: Transfers (2)
Handshaking provides support for multiple clock domains
  Slower devices can stretch the transfer
  No additional delay when agents fast enough
  Mandatory in asynchronous systems
Address
M
Data
S
Read
M
M
Req
S
Ack
1
2
3
4

## Slide 9: Transfers (3)
1. Dedicated bus control signals used for handshaking
Exceptions: * v.1 does not use, v.2 uses
2. Split transfers
3. Pipelined transfers
4. Broadcast support

## Slide 10: Arbitration / Decoding
Arbitration decides which master can use the shared resource (e.g. bus)
  Single-master system does not need arbitration
  E.g. priority, round-robin, TDMA
  Two-level : e.g. TDMA + priority
Decoding is needed to determine the target
  Central / Distributed

## Slide 11: Centralized / Distributed
A2
arbiter/
decoder
A3
arbiter/
decoder
A1
arbiter/
decoder
A4
arbiter/
decoder
A5
arbiter/
decoder
M = master
S = slave
Arbiter
M1
M2
M3
S1
S2
S3
Decoder
a) Centralized
b) Distributed
Figure 2. Centralized vs. distributed control

## Slide 12: Reconfiguration
Not all the communication can be estimated beforehand
  Communication varies dynamically
  Arbitration may perform poorly
Dynamic reconfiguration can be used to change the key parameters
  Communication can be tuned to better meet the current requirements

## Slide 13: Arbitration and reconfiguration
1. Application specific (‘as’), one-level (‘1’) or two-level (‘2’) arbitration scheme
2. Arbitration done during previous transfer (pipelined arbitration)
3. Centralized arbitration (‘C’) or distributed arbitration (‘D’)
4. Dynamic reconfiguration

## Slide 14: Problem1 : Bandwidth
d) split-bus
A
A
A
A
A
A
a) single bus
A
A
A
A
A
A
c) multiple bus
B
A
A
A
A
A
A
b) hierarchical bus
A
A
A
A
A
A
A = Agent
B = Bridge
Figure 3. Bus structures

## Slide 15: Problem 2: Signaling (1)
Estimated edge-to-edge propagation delay of 50nm chips 6-10 cycles
Wires have a notable capacitance
Asynchronous techniques
  E.g. Marble bus
    Four-phase hand-shaking
    Uses two signals for each bit
    ”01” = low, ”10” = high, ”00” and ”11” = illegal
Split-bus technique
  If target is near, only necessary switches are on so that effective wire capacitance is smaller
    smaller power
    parallel transfers
    smaller delay (beneficial in async only)
  More complex arbitration

## Slide 16: Problem 2: Signaling (2)
Latency insensitive protocols
  Long signals lines pipelined with relay stations (r)
  Originally for point-to-point networks
Multiple clock domains
  Globally Asynchronous, Locally Synhronous (GALS)
  Simplifies system design and clock tree generation
  Power saving in global clock is often stated (”hyped”) as main reason
    According to [Malley, ISVLSI,03] GALS may even increase power consumption
    Power saving by lowering frequency of some parts seems more probable
A
A
A
r
r
r
r
r
r

## Slide 17: Problem 2: Signaling (3)
Bus encoding for low power
  Invert data if that reduces signal line activity
  Reported power saving ~25%

## Slide 18: Problem 3: Reliability
Long parallel lines increase fault rate due to
  Crosstalk
  Dynamic delay
Long wires have large coupling capacitance
  Narrow (for high density)
  Thick (for smaller resistance)
Error detection / correction
  Bus coding
  Bus guardians
  Detection+retransfer seems more energy efficient than correction
  Layered approach
See Chapter 6

## Slide 19: Problem 4: Quality-of-service (1)
Guaranteed bandwidth / latency
Arbitration
  Round-robin
    Fair
  Priority
    Min latency for high priorities
    Starvation possible
  Time Division Multiple Access (TDMA)
    Most versatile
    Requires common notion of time
Centralized control favors Qos
  However, scalability (among other reasons) does not favor centralized control

## Slide 20: Problem 4: Quality-of-service (2)
Multiple priorities for data (virtual channels)
  E.g. HIBI supports currently 2 priorities
  Usually requires more buffering
Reconfiguration
  Set priorities, TDMA, etc. at runtime
  Hardest part is to decide when to reconfigure

## Slide 21: Problem5: Interface Standardization
Number of different (incompatible) bus protocols approaches infinity
Virtual Component Interface (VCI)
Open Core Protocol (OCP)
  Derived from VCI
  TUT is a member of OCP
  Masters and slaves
Wrapper ideology
  Translates protocols
Underlying network is ’wrapped’ so that the interface is the same
Agent
System
initiator
IP
Master
VCI /
OCP
Master
Network
wrapper
Agent
System
target
IP
Slave
Slave
Network
wrapper
Agent
System
initiator/target
IP
Master
Master
Network
wrapper
Slave
Slave
HIBI on-chip network
HIBI on-chip network
Any on-chip network

## Slide 22: SoC Examples
Amulet3i by Univ. Manchester
  Asynchronous microcontoller
  A single Marble bus
MoVA by ETRI
  MPEG-4 video codec
  AMBA ASB and APB buses
Viper by Philips
  Set-top box SoC
  Three PI buses and memory bus

## Slide 23: Amulet3i – Asynchronous microcontroller
Amulet 3i
0.35 um
7 x 3.5 mm2
120 MIPS
215 mW @ 85 MHz
Marble bus
Amulet3
core
Instruction
bridge
Data
bridge
RAM
Bus control
Control/test
registers
Synchronous
peripheral bridge
ROM
ADC
DMA
Off-chip
interface
Figure 4. Amulet3i

## Slide 24: MoVA – MPEG-4 codec
MoVA
0.35 um
220k NAND2 gates
412 Kb SRAM
110.25 mm2
Total 1.7 Mgates
3.3 V
0.5 W @ 27 MHz
30 fps QCIF
15 fps CIF
ARM7TDMI
core
AMBA ASB
ROM
I/O
APB
bridge
AMBA APB
Host
I/O
Stream
output
VLC
I/O
Video codec IP (6)
I/O
Video (3)
I/O
SDRAM
I/O
AMBA wrapper
Bus
control (3)
Arbiter &
Decoder
RPC,
INTC
& Timer
Figure 5. MoVA

## Slide 25: Viper – Set-top box SoC
0.18 um
2 processors + 50 cores
Total 8M NAND2 gates
750 Kb SRAM
82 clock domains
1.8 V
4.5 W @143/150/200 MHz
MIPS
Interrupts & JTAG
TM32
General
peripherals (8)
High-speed
interfaces (2)
Audio, video,
and 3D graphics
IP blocks (9)
Other IP blocks (6)
Main
memory interface
Bridge
MIPS
PI-bus
TM32
PI-bus
DVP bus
Bridge
Fast
PI-bus
Bridge
Bridge
Bridge
2D graphics
Audio, video,
and 3D graphics
interfaces (6)
Figure 6. Viper

## Slide 26: HIBI
Heterogeneous IP Block Interconnection
Developed at TUT
Hierarchical bus NoC
Parameterizable, scalable
QoS
Run-time reconfiguration
Efficient protocol
Automated communication-centric design flow

## Slide 27: HIBI Network Example
Clock domain
HIBI
Wrapper
IP BLOCK
Bridge
HIBI
Wrapper
HIBI
Wrapper
IP BLOCK
HIBI
Wrapper
HIBI
Wrapper
HIBI
Wrapper
HIBI
Wrapper
IP BLOCK
HIBI
Wrapper
IP BLOCK
HIBI
Wrapper
IP BLOCK
HIBI
Wrapper
IP BLOCK
HIBI
Wrapper
IP BLOCK
HIBI
Wrapper
HIBI
Wrapper
IP BLOCK
HIBI
Wrapper
IP BLOCK
IP BLOCK
HIBI
Wrapper
Figure 7. Example of hierachical HIBI
Notes: ANIMAATIO

## Slide 28: H.263 Video Encoder
Objective: Show how easily HIBI scales
2-10 ARM7 processors
Processor independent C-source code
Master + scaleable number of processors generated automatically
Verified with HW/SW co-simulation
I/O
HIBI Wrapper
H.263
YUV
ARM7 + DMA
HIBI Wrapper
ARM7 + DMA
HIBI Wrapper
MASTER
HIBI Wrapper
ARM7 + DMA
…
SLAVES
DMA
DPRAM
ROM
ARM7
Figure 8. HIBI-based H.263 codec
Notes: <number>
<footer>
<header>
<date/time>
Mpeg-4 simple profile
HUOM! Tässä on korostettava, että sovellus sopii SoCille mutta on luonteeltaan multiprosessori (katso extra-kalvo lopusta)

## Slide 29: Conclusions
No general network suits every application
Ratio between achieved and maximum throughput is small
Heterogenous network addresses these problems
  Local and global communication separated
  Use bus for local communication
  Application specific network for global communication

## Slide 30: References
D. Sylvester and K. Keutzer, “Impact of small process geometries on microarchitectures in systems on a chip,” Proceedings of the IEEE, Vol. 89, No. 4, Apr. 2001, pp. 467-489.
P. Wielage and K. Goossens “Networks on silicon: blessing or nightmare?,” Symp. Digital system design, Dortmund, Germany, 4-6 Sep. 2002, pp. 196-200.
R. Ho, K.W. Mai, and M.A. Horowitz, “The future of wires,” Proceedings of the IEEE, Vol. 89, No. 4, Apr. 2001, pp. 490-504.
D.B. Gustavson, “Computer buses a tutorial,” in Advanced multiprocessor bus architectures, Janusz Zalewski (ed.), IEEE Computer society press, 1995. pp. 10-25.
ARM, AMBA Specification Rev 2.0, ARM Limited, 1999.
IBM, 32-bit Processor local bus architecture specification, Version 2.9, IBM Corporation, 2001.
B. Cordan, “An efficient bus architecture for system-on-chip design,” IEEE Custom integrated circuits conference, San Diego, California, 16-19 May 1999, pp. 623-626.
K. Kuusilinna et. al., “Low latency interconnection for IP-block based multimedia chips,” IASTED Int’l conf. Parallel and distributed computing and networks, Brisbane, Australia,14-16 Dec. 1998, pp. 411-416.
V. Lahtinen et. al., “Interconnection scheme for continuous-media systems-on-a-chip,” Microprocessors and microsystems, Vol. 26, No. 3, April 2002, pp. 123-138.
W.J. Bainbridge and S.B. Furber, “MARBLE: an asynchronous on-chip macrocell bus,” Microprocessors and microsystems, Vol. 24, No. 4, Aug. 2000, pp. 213-222.
OMI, PI-bus VHDL toolkit, Version 3.1, Open microprocessor systems initiative, 1997.
Sonics, Sonics Networks technical overview, Sonics inc., June 2000.
B. Ackland et. al., “A single-chip, 1.6-billion, 16-b MAC/s multiprocessor DSP,” IEEE Journal of solid state circuits, Vol. 35, No. 3, Mar. 2000, pp. 412-424.
14. Silicore, Wishbone system-on-chip (SoC) interconnection architecture for portable IP cores, Revision: B.1, Silicore corporation, 2001.
E. Salminen et. al., “Overview of Bus-based System-on-Chip Interconnections,” Int’l symp. Circuits and systems, Scottsdale, Arizona, 26-29 May 2002, pp. II-372-II-375.
S. Dutta, R. Jensen, and A. Rieckmann, “Viper: a multiprocessor SoC for advanced set-top box and digital TV systems,” IEEE Design and test of computers, Vol. 8, No. 5, Sep./Oct. 2001, pp. 21-31.
K. Lahiri, A. Raghunathan, and G. Lakshminarayana, “Lotterybus: a new highperformance communication architecture for system-on-chip designs,” Design automation conference, Las Vegas, Nevada, 18-22 June 2001, pp. 15-20.
VSIA, Virtual component interface specification (OCB 2 1.0), VSI alliance, 1999.
OCP international partnership, Open core protocol specification, release 1.0, OCP-IP association, 2001.
L. Benini and G. De Micheli, “Networks on chips: a new SoC paradigm,” Computer, Vol. 35, No. 1, Jan. 2002, pp. 70-78.
A. Boxer, “Where buses cannot go,” IEEE Spectrum, Vol. 32, No. 2, Feb. 1995, pp. 41-45. 22. L.P. Carloni and A.L. Sangiovanni-Vincentelli, “Coping with latency in SoC design,”
IEEE Micro, Vol. 22, No. 5, Sep./Oct. 2002, pp. 24-35.
Cheng-Ta Hsieh and M. Pedram, “Architectural energy optimization by bus splitting,” IEEE Transactions on computer-aided design of integrated circuits and systems, Vol. 21, No. 4, Apr. 2002, pp. 408-414.
M.R. Stan and W.P. Burleson, “Bus-invert coding for low-power I/O,” IEEE Transactions on very large scale integration (VLSI) systems, Vol. 3, No. 1, Mar. 1995, pp. 49-58.
M. Lajolo, “Bus guardians: an effective solution for online detection and correction of faults affecting system-on-chip buses,” IEEE Transactions on very large scale integration (VLSI) systems, Vol. 9, No. 6, Dec. 2001, pp. 974-982.
A.B. Kahng, S. Muddu, and E. Sarto, “Interconnect optimization strategies for highperformance VLSI designs,” Int’l conf. VLSI design, Goa, India, 7-10 Jan. 1999, pp. 464-469.
W.O. Cesario et. al., “Multiprocessor SoC platforms: a component-based design approach,” IEEE Design and test of computers, Vol. 19, No. 6, Nov./Dec. 2002, pp. 52-63.
J.D. Garside et. al., “AMULET3i - an asyncronous system-on-chip,” Int’l symp. Advanced research in asynchronous circuits and systems, Eilat, Israel, 2-6 Apr. 2000, pp. 162-175.
J.H. Park et. al., “MPEG-4 Video codec on an ARM core and AMBA,” Works. MPEG-4,San Jose, California, 18-20 June 2001, pp. 95-98.